## Slide 1: Welcome to CS220A: Computer Organization
Mainak Chaudhuri
Indian Institute of Technology Kanpur

## Slide 2: Sketch
The computing stack
Anatomy of a computer system

## Slide 3: The computing stack
Microarchitecture
Function blocks
Logic gates
Circuits
Transistors
Hardware
HLL compiler
Assembly language
Assembler and linker
Executable binary
Operating system
Hardware/
software
interface
Problem
Algorithm
HLL program
Software
CS220A
ESC201N
ESC101N

## Slide 4: Logic gates to microarchitecture
Example of a ripple-carry adder
  Logic gates for building a function block for adding two bits with a carry input
    Known as a full adder
  An array of full adders used to design the microarchitecture of an adder
    Encapsulates an algorithm for adding two n-bit numbers
    A microarchitecture is always linked to an underlying algorithm for executing the task
A digital computer represents one of the most complex pieces of microarchitecture
  A complex algorithm implemented in hardware

## Slide 5: Anatomy of a computer system
Instruction Processor
or
CPU
I/O devices and non-volatile storage
Main memory (DRAM)

## Slide 6: Anatomy of a computer system
The central processing unit (CPU)
  Also known as microprocessor
  Dictates how a task will be done, but cannot do anything on its own
  Needs to be told what to do next in the form of a stream of “instructions”
    These instructions are generated from a program that represents an algorithm for accomplishing the task
  Can store intermediate/final results of a computation in main memory
    Dynamic random access memory (DRAM); volatile
  Can store information on persistent non-volatile storage media e.g., magnetic hard disk

## Slide 7: Anatomy of a computer system
Peripheral I/O devices
  Plug-ins to the CPU for communicating with the world
  Display (CRT, LCD, touchscreen)
  Keyboard
  Mouse
  DVD reader/writer
  Speaker
  Microphone
  Camera
  Wireless communication
  Wired Ethernet communication

## Slide 8: Anatomy of a computer system
How does an instruction execute inside the processor?
  Every entity residing inside a computer has an address
    An instruction also has an address
  The processor maintains the address of the next instruction in a register called program counter
  The instruction is fetched from main memory and placed in an instruction register
  The instruction is decoded to generate the control signals for executing the instruction
    Send to adder if this is an addition instruction

## Slide 9: Anatomy of a computer system
How does an instruction execute inside the processor?
  Most instructions require source operands for execution
    a+b
  After decoding the instruction, the operands are fetched
    Operand addresses are typically encoded in the instruction or could be implicit
    These addresses are known after decoding the instruction
  The instruction can now execute
    Operands are sent to the adder

## Slide 10: Anatomy of a computer system
How does an instruction execute inside the processor?
  Most instructions generate a result
    c=a+b
  The address of the result (or destination) operand is typically encoded in the instruction or implicit
    This address is known after decoding the instruction
  The result is stored in the destination operand location

## Slide 11: Anatomy of a computer system
How does an instruction execute inside the processor?
  The execution of an instruction requires the appropriate control and data paths to be activated
Data path is usually slow because main memory is much slower than the processor
  Commonly used optimizations for speeding up the data path:
    Reasonably large set of general-purpose registers inside the processor
    Fast memory (known as cache) inside the processor