## Slide 1: Processor FSM Design
Mainak Chaudhuri
Indian Institute of Technology Kanpur

## Slide 2: Sketch
Abstract model of computer
Single-cycle instruction execution
Multi-cycle instruction execution
Pipelined instruction execution

## Slide 3: Abstract model of computer
Each instruction undergoes five stages
  Stage 0 (IF): fetch the instruction pointed to by program counter from memory
  Stage 1 (ID/RF): decode the instruction to extract various fields and read source register operands
    Source registers can be read in parallel with instruction decoding in MIPS due to fixed positions of rs and rt in all formats of the ISA
  Stage 2 (EX): execute the instruction in ALU; compute address of load/store instructions; update program counter to PC+4 or branch target (if this instruction is control transfer ins)
  Stage 3 (MEM): access memory if load/store instruction; use address computed in stage 2
  Stage 4 (WB): write result back to destination register if the instruction produces a result

## Slide 4: Single-cycle instruction execution
Possible to implement all five stages as a big combinational logic
  All the memory elements are also combinational meaning that the input address can be presented any time within a cycle and the output data is available within the same cycle
    Register file (in stages 1 and 4), icache (in stage 0), and dcache (in stage 3) are the combinational memory elements
    PC, icache[PC], reg[rs], reg[rt], dcache[disp(rs)] are inputs
      dcache[disp(rs)] is a relevant input for loads
    PC, reg[rd] or reg[rt], dcache[disp(rs)] are outputs
      dcache[disp(rs)] is a relevant output for stores
  The instruction opcode and function (for R format) fields decide the control of combinational logic e.g., which register operand(s) is/are valid sources, which ALU operation to invoke, etc.

## Slide 5: Single-cycle instruction execution
Combinational logic
PC
ICACHE
DCACHE
REGFILE
Taken branch ? Branch target : PC + 4
instruction
sext(disp) +
reg[rs]
reg[rt]
load
data
instruction result
r/w ports: rs, rt, rd
reg[rs]
reg[rt]
clk

## Slide 6: Single-cycle instruction execution
Taken branch
  A branch instruction whose condition dictates that the next instruction to be executed is the one at the branch target
    beq $1, $2, label (the branch is taken if $1 == $2)
    Unconditional direct and indirect jumps and procedure calls are always taken branches
Not taken branch
  A branch instruction whose condition dictates that the next instruction to be executed is the instruction right next to the branch
    A la Frost’s “Road Not Taken”
    beq $1, $2, label (the branch is not taken if $1 != $2)
    A conditional branch can be taken or not taken depending on how the condition evaluates at run time

## Slide 7: Single-cycle instruction execution
PC
Icache
RF
Ext.
IR
Add
ALU
Dcache
4
w
r
r
=?
IF
ID/RF
EX
MEM
WB
CLK
Cond.br. target in MIPS:
PC+4+(sext(offset)<<2)
reg[rt]
(store data)
reg[rs]
load
data
Addr.
instruction result

## Slide 8: Single-cycle instruction execution
Clock cycle time must be large enough to accommodate the lengthiest instruction
  This is typically the load instruction whose critical path includes all five stages: IF: fetch instruction, ID/RF: decode while reading reg[rs] and sign extending displacement, EX: add reg[rs] with sext(disp) to generate address, MEM: read dcache to get load data, WB: write load data back to reg[rt]
  Not a good idea since many other instructions take smaller amount of time
    Control transfer instructions require only three stages
    Stores require only four stages
    All ALU instructions can bypass MEM stage

## Slide 9: Multi-cycle instruction execution
Each stage takes one cycle to execute
  Processor is now a five state FSM and the memory elements are sequential
  Need flip-flops at stage boundaries and each stage is a combinational logic
  Clock cycle time = latency of the longest stage
  Most instructions take five cycles
    ALU instructions do nothing in MEM stage, but will have to go through it if FSM state transition is implemented using an incrementer
    Some instructions may take longer e.g., multiply/divide, load/store (in case of dcache miss)
    Some instructions may take shorter time e.g., stores take four cycles, control transfer instructions take three cycles
  Overall CPI depends on instruction mix

## Slide 10: Multi-cycle instruction execution
Example
  IF: 2 ns, ID/RF: 1 ns, EX: 1 ns, DMEM: 3 ns, WB: 1 ns
  Branch frequency: 20%
  Store frequency: 10%
  Multiply/divide frequency: 5%, latency: 30 ns
  Total instruction count: 100
Multi-cycle
  Cycle time: 3 ns, frequency: 333 MHz
  CPI: 0.2*3+0.1*4+0.05*10+0.65*5 = 4.75
  Execution time: 100*4.75*3 ns = 1425 ns
Single-cycle
  Cycle time: 8 ns, frequency: 125 MHz
  CPI: 1*0.95+ceil(30/8)*0.05 = 1.15
  Execution time: 100*1.15*8 ns = 920 ns

## Slide 11: Multi-cycle instruction execution
Same example with a balanced pipeline
  IF: 2 ns, ID/RF: 2 ns, EX: 2 ns, DMEM: 2 ns, WB: 2 ns
  Branch frequency: 20%
  Store frequency: 10%
  Multiply/divide frequency: 5%, latency: 30 ns
  Total instruction count: 100
Multi-cycle
  Cycle time: 2 ns, frequency: 500 MHz
  CPI: 0.2*3+0.1*4+0.05*15+0.65*5 = 5
  Execution time: 100*5*2 ns = 1000 ns
Single-cycle
  Cycle time: 10 ns, frequency: 100 MHz
  CPI: 1*0.95+ceil(30/10)*0.05 = 1.1
  Execution time: 100*1.1*10 ns = 1100 ns (worse than multi-cycle)

## Slide 12: Pipelined instruction execution
Observations from multi-cycle design
  In the second cycle, I know if it is a branch; if not, start fetching the next instruction?
  When the ALU is doing an addition (say), the decoder is sitting idle; can we use it for some other instruction?
  In summary, exactly one stage is active at any point in time: wastes hardware resources
Form a pipeline
  Process five instructions in parallel
  Each instruction is in a different stage of processing (called pipe stage)

## Slide 13: Pipelined instruction execution
Individual instruction latency is five cycles, but ideally can finish one instruction every cycle after the pipeline is filled up
  Ideal CPI of 1.0 at the clock frequency of multi-cycle design
  Execution time is ideally one-fifth of the multi-cycle design
    Instruction throughput improves five times (number of instructions completed in a given time)
    I0 IF ID/RF EX MEM WB
    I1 IF ID/RF EX MEM WB
    I2 IF ID/RF EX MEM WB
    I3 IF ID/RF EX MEM WB
    I4 IF ID/RF EX MEM
time

## Slide 14: Pipelined instruction execution
Gains
  Extracting parallelism from a sequential instruction stream: known as instruction-level parallelism (ILP)
  Can complete one instruction every cycle (ideally)
Loss
  Each pipe stage may get lengthened a little bit due to control overhead (skew time, setup time, propagation delay): limits the gain due to pipelining
  Each instruction may take slightly longer for this reason
  Bigger aggregate memory bandwidth: icache and dcache may miss in the same cycle
  Pipeline hazards

## Slide 15: Pipeline hazards: structural
Structural hazards
  Arises due to resource conflicts
  Happens if the same resource is accessed in at least two stages of the pipe
  Fewer resources than needed
  Unpipelined functional units
  Lack of memory or register file ports
Why fewer resources?
  Reduction in complexity (and power consumption)
  Make the common case fast: pipelined divider may only waste silicon estate
All types of hazards introduce stalls or pipeline bubbles

## Slide 16: Pipeline hazard: control
Branches pose a problem
Cycles
ins i (beq $1, $0, label) IF ID/RF EX MEM WB
What to fetch? IF
What to fetch? IF
ins i+1 (target) IF
Two pipeline bubbles: increases average CPI
Can we reduce it to one bubble?

## Slide 17: Branch delay slot
MIPS R3000 has one bubble
  Called branch delay slot
  Exploit clock cycle phases
  On the positive half compute branch condition
  On the negative half fetch the target
beq $1, $0,label IF ID EX MEM WB
Bubble IF
Target IF
The PC update hardware (selection between target and next PC) works on the lower edge

## Slide 18: Branch delay slot
Can we utilize the branch delay slot?
  The delay slot is always executed (irrespective of the fate of the branch)
    Reason why branch target is PC+4+(sext(offset)<<2)
  Boost instructions common to fall through and target paths to the delay slot or from earlier than the branch
  if (cond) { branch instruction
  // fall through delay slot
  }
  else {
  // target
  }

## Slide 19: Branch delay slot
Can we utilize the branch delay slot?
  Boost instructions common to fall through and target paths to the delay slot or from earlier than the branch
  Not always possible to find
  Must boost something that does not alter the outcome of the computation
  If the BD slot is filled with useful instruction then we don’t lose anything in CPI; otherwise we pay a branch penalty of one cycle

## Slide 20: Branch prediction
To increase the clock frequency, designers may choose a deeper pipeline
  Subdivide the longest stage further
If the number of pipe stages increases between IF and EX, branch penalty also increases
  Pipe1: IF ID/RF EX … Br. penalty?
  Pipe2: IF ID RF EX … Br. penalty?
  Pipe3: IF1 IF2 ID RF1 RF2 EX … Br. penalty?
  Assume no branch delay slot
    Meaning that IF or EX cannot be accommodated in half cycle

## Slide 21: Branch prediction
To increase the clock frequency, designers may choose a deeper pipeline
  Subdivide the longest stage further
If the number of pipe stages increases between IF and EX, branch penalty also increases
Today all processors rely on branch predictors that observe the behavior of individual branches and learn to predict their future behavior
  Makes it possible to infer the next instruction’s PC even before the branch executes
  Pipeline must be flushed on a wrong prediction

## Slide 22: Branch target buffer
Branch target buffer
  We can put a branch target cache in the fetcher
  Also called branch target buffer (BTB)
  Use the lower bits of the instruction PC to index the BTB
  Use the remaining bits to match the tag
  In case of a hit the BTB tells you the target of the branch when it executed last time
  You can hope that this is correct and start fetching from that predicted target provided by the BTB
  Later you get the real target, compare with the predicted target, and throw away the fetched instruction in case of misprediction; keep going if predicted correctly

## Slide 23: Branch target buffer
BTB is looked up with the PC of every instruction in parallel with fetching the instruction
  On a hit, it provides two pieces of information: this instruction is a control transfer instruction and the target of this control transfer instruction seen last time
    This target will be used to fetch in the next cycle
  On a miss, the fetcher has no option but to fetch from the fall through path (PC+4) in the next cycle
  A control transfer instruction is inserted in the BTB after the EX stage when its target is known
    A lookup at this point may hit in the BTB; if the branch is not taken, the BTB entry is invalidated; otherwise the entry is updated with the taken target
    If a lookup at this point misses in the BTB, a new entry is allocated provided the branch is taken

## Slide 24: Branch target buffer
Assume for a program
  90% of all control transfer instructions hit in the BTB
  90% of outcomes provided by BTB hits are correct
  20% of control transfer instructions that miss in the BTB result in taken branches
  Fraction of bubbles saved = BTB prediction accuracy = 0.9*0.9+0.1*0.8 = 0.89
  11% branches suffer from mispredictions and will require some “recovery” mechanism for correct execution

## Slide 25: Branch prediction
BTB will work great for
  Loop branches (how many misprediction?)
  Subroutine calls
  Unconditional branches
What about jalr ?
Conditional branch prediction
  Rather dynamic in nature
  The last target is not very helpful in general (if-then-else)
  Need a direction predictor (predicts taken or not taken)
  Once that prediction is available we can compute the target

## Slide 26: Direction predictors
How about static prediction?
  Always not-taken (NT) or always taken (T): penalty?
  Forward not-taken and backward taken (rationale?)
Deeper pipelines
  Define branch penalty
  Big problem: deeper pipelines increase branch penalty
  Must have better branch predictors for deeper pipeline

## Slide 27: Control dependence
Roughly every fifth instruction is a branch
  Need to be on the right control flow path
    This is the source of input to the pipeline
  Static techniques are not enough
    Need highly accurate dynamic predictors
  Speculate past branches: Alpha 21264 allows 20 outstanding branches, MIPS R10000 allows only 4
    Need to speculate past predicted branches in deeper pipelines (not a big issue in five-stage pipe)
  Prediction accuracy?
    Probability of a correct prediction is p
    Probability of staying on correct path after n predictions pn
    What is minimum p if n is 4 (MIPS R10k)? If n is 20?

## Slide 28: Direction predictors
Let us encode each taken branch as 1 and not taken branch as 0
  The behavior of a conditional branch can be represented as a binary string
  Loop branch: 11111…110
  Alternating if-else: 1010101010 or 0101010101
  If-else branches can exhibit a wide variety of patterns

## Slide 29: Direction predictors
The problem of direction prediction is essentially design of an estimator that, given an n-bit history, tells us the next most likely outcome for a particular static branch instruction
  All branch predictors compute the probability of seeing a zero or one, given the recent pattern history h of some limited length n
  Suppose the number of time 0 appears after h is C0 and similarly define C1; the prediction is 1 if C1 >= C0 and 0 otherwise
    Instead of having two counters, C1-C0 is maintained

## Slide 30: Direction predictors
Let the difference counter be C(h) for a certain history h: C(h) = C1(h) – C0(h)
  Let C(h) be of k bits length (this is independent of the history length)
  Can count from 0 to 2k -1
  On seeing 0 after h, decrement C(h); on seeing 1 after h, increment C(h)
  Saturates at boundaries (a saturating counter)
    Does not decrement below 0 or increment above 2k -1
  By examining C(h) at any point in time, we can say which outcome had higher likelihood in the last 2k occurrences of history h
    Need to shift the origin to mid-point 2k-1
    If C(h) is below mid-point, the prediction is zero; otherwise 1

## Slide 31: Direction predictors
C(h)
h
H(Branch PC)
Branch history table
Counter table
n
k
2n
111001010

## Slide 32: Direction predictors
How many different histories? [Size of BHT]
  No history? [no BHT] Two possible designs:
    Just a global counter that counts occurrences of 0’s and 1’s and offers prediction based on that
      Not very useful
    One counter per branch (known as bimodal predictor)
      Somewhat useful: helps identify largely bimodal distributions
  One global history? [Size of BHT = 1]
    Captures cross-correlation between branches
    Since history is a sliding pattern, h will keep on changing
      One counter for each history pattern? Use a hashmap
  One local history per branch? Size of BHT?
    Hash history patterns to counters
    Loses global correlation

## Slide 33: Bimodal predictors
C(h)
h
H(Branch PC)
Branch history table
Counter table
n
k
2n
111001010

## Slide 34: Bimodal predictors
C
H(Branch PC)
Pattern history table (PHT)
k
2n
Predicted NT if
less than 2k-1

## Slide 35: Bimodal predictors
Simplest of the lot (used in MIPS R10000)
  Maintains a pattern history table (PHT)
    MIPS called it a branch history table (BHT)
  Each entry is a saturating counter
  Basic idea is to go with the most frequent pattern seen in the past
  How do you index it?
  Aliasing?
  How wide is each counter?
  Performance of loops (simplest kind of control flow)
  Alternating branches?
  Correlating branches?

## Slide 36: Challenges
Aliasing in pattern history table
  Multiple branches mapping to the same counter
Height of pattern history table is exponential in history length
  Need long history for better prediction
  Neural predictors help
What are the best ways to combine multiple predictors?
  Each predictor can be an expert for a certain type of branch

## Slide 37: Pipeline hazard: data
Pipelining disturbs the sequential thought-process
  Data dependencies among instructions start to show up
  add $1, $2, $3
  sub $4, $1, $5
  and $6, $1, $7
  or $8, $1, $9
  xor $10, $1, $11
  Result of add is needed by all instructions (RAW hazard: read after write hazard)
  add IF ID EX MEM WB
  sub IF ID EX MEM WB
  and IF ID EX MEM WB
  or IF ID EX MEM WB
  xor IF ID EX MEM WB

## Slide 38: Pipeline hazard: data
How to avoid increasing CPI?
  Stalling is clearly not acceptable
  Phased register file solves three-cycle apart RAW
  Can we forward the correct value just in time?
  add IF ID EX MEM WB
  sub IF ID EX MEM WB
  and IF ID EX MEM WB
  Read wrong value in ID/RF, but bypassed value overrides it (need a multiplexor for each ALU input to choose between the RF value and the bypassed value)

## Slide 39: Data hazards
MEM/WB to MEM bypass
  add r1, r2, r3
  lw r4, 0(r1)
  sw r4, 20(r1)
  add IF ID EX MEM WB
  lw IF ID EX MEM WB
  sw IF ID EX MEM WB

## Slide 40: Pipeline hazard: data
Can we always avoid stalling?
  lw $1, 0($2)
  sub $4, $1, $5
  and $6, $1, $7
  or $8, $1, $9
  lw IF ID EX MEM WB
  sub IF ID EX MEM WB
  and IF ID EX MEM WB
  or IF ID EX MEM WB
  Need some time travel (backwards)! Not yet feasible!!
  One option: hardware pipeline interlock to stall the sub by a cycle
  Early generations of MIPS (Microprocessor without Interlocked Pipe Stages) had the compiler to fill the load delay slot with something independent or a NOP

## Slide 41: Hiding data hazard stalls
In general, cache misses for load instructions can introduce large stalls in the pipeline
Some of the established ways to hide some of these stalls
  Execute instructions that do not depend on the load instruction that has missed in the cache
    Requires ways to reorder the instruction sequence inside the processor
  Prefetch data into cache before it is needed
    Need to predict the sequence of data addresses and prefetch from memory hierarchy based on the prediction
  Predict return value of the load instruction even before it executes

## Slide 42: Pipelined instruction execution
All three types of hazards can cause pipeline stalls and introduce bubbles in the pipeline depending on the pipeline organization
Overall speedup of pipelining over multi-cycle non-pipelined implementation = number of pipe stages/(1 + average stall cycles per instruction)