## Slide 1: Basics of Digital Logic Design
Mainak Chaudhuri
Indian Institute of Technology Kanpur

## Slide 2: Sketch
Combinational logic
Sequential logic
Field programmable gate array
Asynchronous inputs
Static random access memory (SRAM)
Dynamic random access memory (DRAM)
Finite state machines

## Slide 3: Combinational logic
No memory for remembering state
Usually always enabled
Some important combinational logic units
  Decoders
  Multiplexors
  Encoders
  Priority encoders
  Comparators
Any combinational logic can be designed using AND, OR, and NOT gates
  CMOS: NAND, NOR, and NOT gates

## Slide 4: Combinational logic
Two-level logic implementation
  Any combinational logic can be designed by having an array of AND gates in first level, an array of OR gates in the second level, and an optional NOT to get the output
    Sum of product (SoP) representation; sum of minterms
  First level OR and next level AND
    Product of sum (PoS) representation; product of maxterms
  SoP and PoS representations follow directly from the truth table
  Example: full adder

## Slide 5: Combinational logic
Programmable logic array (PLA)
  Another name for SoP implementation
  AND plane and OR plane
  Size of the planes?
  Dot representation
Implementing Boolean functions in ROM
  Read only memory
    PROM and EEPROM variants
  Number of rows is exponential in number of inputs
  Number of columns is equal to number of functions

## Slide 6: Combinational logic
Comparison between ROM and PLA for implementing combinational logic
  ROM requires a full decoder (array of AND gates)
  The AND plane size of PLA depends on the number of distinct minterms across all outputs
  As the number of inputs grows, ROM height grows exponentially; PLA size grows slowly
Logic minimization
  Critical for good designs
  Karnaugh map (K map) is useful for understanding the manual process
  Tedious for large designs; usually automated

## Slide 7: Sequential logic
Computation proceeds in discrete steps
  Computation in a step may depend on the states in the previous step
    Requires storage or memory
  A signal must define what a step is
    This is the clock signal
  Edge-triggered logic changes the states on a clock edge
    Input to a state storage is sampled on the clock edge
    After the propagation delay through the state element, the input appears on the output
    Rising edge (posedge) or falling edge (negedge)
  Sequential logic doesn’t compute, it helps implement storage

## Slide 8: Why sequential logic
Results produced by combinational logic needs to be stored
Also, inputs to combinational logic typically come from storage
  Computation begins with stored inputs and ends with stored outputs
Output of the combinational logic gets sampled at the clock edge (rising or falling)
  The output must be valid by now
  Needs to be stored before output changes
  Dictates a lower bound on clock cycle time
    Latency of combinational logic

## Slide 9: Why sequential logic
f
y
x
clk
≥ Latency of f
synchronous computation

## Slide 10: Storage/State elements
Usually known as memory elements
  Latches, flip-flops, register files
  Latches are usually level-sensitive
    SR latch (set-reset latch) does not have a clock input
      Cross-coupled NOR gates
  Flip-flops are edge-triggered
    Always has a clock input
    Setup time and hold time for input data
    Propagation delay to output (clock-to-Q delay)
    Cycle time is at least the sum of propagation delay, combinational logic delay, setup time, and clock skew
      Reduce clock skew by careful clock routing
    Edge-triggering requires more logic; can be slow

## Slide 11: Storage/State elements
Handling clock skew
  Lengthening the cycle time by the skew time (as discussed in the previous slide) guards against the situation where clock at y arrives before x
    Since the cycle time has been lengthened by skew time, the input to y would be ready by within cycle time – skew time
  Lengthening the cycle time alone is not enough if the clock at y arrives after x
    In this case, an error occurs if skew time is more than propagation delay + min delay through f + setup time
    The error is that y will not be able to store the result of the last computation
    Edge at x needs to be delayed by adding logic

## Slide 12: Delayed clock to handle skew
f
y
x
clk
Delay=skew time
Need to identify the paths where such delay should be inserted.
This is done in addition to lengthening the cycle time by skew time.

## Slide 13: Storage/State elements
Level-sensitive sequential logic
  A changing input when the clock is high affects the output
  Tricky to design because of race through in an array of combinational computations separated by latches
  Use of two-phase clocks
    Divide combinational logic into two parts
    Clock one part with one phase and another with the other phase
    Alternating phases in the array

## Slide 14: Register file
Array of registers
  A register can be built with an array of flip-flops
  Read ports and write ports
    Input busses for passing register numbers to be read, register number to be written to, data to be written to
    Output busses carrying the read values
  Write enable
    An input that serves as the clock
  Reading requires big multiplexors per port
  Writing requires a decoder per port
  Reading is combinational, writing is sequential
  Improving read latency requires different design

## Slide 15: FPGA
Two-dimensional array of generic logic/storage cells interconnected by programmable switches
  Each cell can be programmed to carry out simple combinational functions
  The interconnection switches can be programmed to realize complex logic where the programmed array works together
  Typically the programming bits are downloaded to the FPGA and the circuit is ready
    Done in the field as opposed to in the fabrication facility; hence the name FPGA

## Slide 16: Field-programmable gate array
Image source: Chu. FPGA Prototyping by Verilog Examples

## Slide 17: Xilinx Spartan 3E FPGA
A 2D array of configurable logic blocks (CLBs)
  Each CLB has four logic/memory slices
  Each of the two logic slices (SLICEL) has
    Two four-input 16-entry look-up table (LUT) function generators (can store any four-input function)
    Two registers
    Two multiplexors
    Arithmetic logic and carry (two full adders)
  Each of the two memory slices (SLICEM) has
    Everything of a logic slice
    Two 16-bit memory blocks (RAM16)
    Two 16-bit shift registers (SRL16)

## Slide 18: Xilinx Spartan 3E FPGA
Image source: Xilinx

## Slide 19: Xilinx Spartan 3E FPGA
Image source: Xilinx

## Slide 20: Xilinx Spartan 3E FPGA
Image source: Xilinx

## Slide 21: Xilinx Spartan 3E FPGA
Image source: Xilinx

## Slide 22: Xilinx Spartan 3E FPGA
A 2D array of configurable logic blocks (CLBs)
I/O blocks (IOB)
  Controls I/O between logic/storage and the user interfaces (slide switches, LEDs, LCD, etc.)
Block RAM (random access memory)
  Each block can store 18K bits
Multiplier blocks
  Each multiplier operates on two 18-bit inputs
Digital clock manager (DCM)
  Routes clock throughout the FPGA

## Slide 23: Xilinx Spartan 3E FPGA
Image source: Xilinx

## Slide 24: Xilinx Spartan 3E FPGA
Five family members
  100K, 250K, 500K, 1200K, and 1600K logic gates
  Specs of XC3S500E
    500K gates
    1164 CLBs (4656 slices); 46 rows, 34 columns
    Some CLB rows and columns are taken up by block RAM, multiplier blocks, DCM
    360K-bit block RAM (20 RAM blocks, each 18K bits)
    20 multiplier blocks
    4 DCMs

## Slide 25: Asynchronous inputs
Asynchronous inputs to a flip-flop may arrive at any time
  Signals coming from outside the computer
  It may be necessary to convert it to a synchronous signal that changes with clock
    Otherwise cannot be used correctly in computation
  Easy way is to pass it through a D flip-flop and use the output of the flip-flop in computation
    Called a synchronizer
    Output will change with clock edge and the output is synchronous with the clock (after propagation delay)
    Fails if the asynchronous input violates setup and hold times

## Slide 26: Asynchronous inputs
Synchronizer failure
  If the asynchronous input changes within the setup time + hold time window around the clock edge, the flip-flop may go into a metastable state (neither 0 nor 1)
    It may take some time for the flip-flop to come out of the metastable state; during this time, the output cannot be used in any computation
  Sample output after sufficient delay so that metastability is resolved with high probability
Synchronizer with two D flip-flops in a chain
  Works if metastability period is smaller than clock period

## Slide 27: Static random access memory
Static random access memory (SRAM)
  Name of a technology used for building reasonably large (up to tens of megabytes) and fast memory
    Register files are much smaller and faster
  Specified as height x width
    4M x 8 bits
  Address, chip select, output enable, write enable, and write data are inputs
  Read data is the output

## Slide 28: Static random access memory
Reading from SRAM
  Chip select should be asserted for reading from or writing to an SRAM chip
  Address is decoded to select a row of SRAM
  The data in the row are read out; called a word
  The read out word appears on the output when output enable is asserted
    Without output enable, the output remains in high impedance state
    Allows tying multiple chips’ outputs to the same data bus with the assumption that exactly one chip’s output enable will be asserted at a time

## Slide 29: Static random access memory
Writing to SRAM
  Chip select should be asserted
  Write enable should be asserted
    It is a narrow pulse
  Data to be written should be on the input data bus
  Address is decoded and the data is written to the appropriate row

## Slide 30: Static random access memory
Building an SRAM
  Address decoder’s outputs are called wordlines
    Each wordline “enables” a row for a read or a write
  Each bit is implemented as two cross-coupled inverters along with additional logic to “hold” the stored charge
    Stored charge (or lack of charge) in a bit represents 1 or 0
    Without this additional logic, the stored charge in a HIGH bit may leak out slowly leading to loss of memory
  The bits of a column are tied together to a single wire called bitline through a per-bit “switch”

## Slide 31: Static random access memory
Building an SRAM
  The bitlines connect to the output bus through tri-state switches
    The tri-state switches are enabled/disabled by the output enable signal
  The write enable pulse can be ANDed with the wordline to act as the “clock” for the row to be written to

## Slide 32: Static random access memory
Building an SRAM
  Very large SRAMs are not built like one big memory due to the large size of the decoder
    Divided into multiple chips that can operate in parallel
    Each chip is said to form a bank
    4M x 8 could be built as eight 4K x 1024 chips
    Entire address is now split into row address and column address
    Possible to also operate only a subset of chips by driving the chip select using certain address bits e.g., 4M x 8 could be built using two “ranks” of eight 2K x 1024 chips (could use address MSB as chip select)
SRAM is used to build fast memory (register file, caches, etc.) inside the processor chip

## Slide 33: Dynamic random access memory
Dynamic vs. static
  Random access memory: can access any location by providing an address
  Static if the charge stored in a bit does not have to be “refreshed” periodically
  Dynamic if the charge needs to be “refreshed” periodically
    DRAM contents can leak away if left to itself for sufficient amount of time
    Each bit is implemented as a capacitor which slowly discharges to ground through “sneak” paths
    The charge must be refreshed periodically
    Refreshing is done in bulk and during refresh data cannot be accessed

## Slide 34: Dynamic random access memory
DRAM
  Why each bit is just a capacitor (implemented using a single transistor)?
    Additional logic reduces the density of storage (number of bits per unit area)
  Density is a very important property of DRAM
  Refreshing is done row by row
    Involves reading out a row and writing the contents back to the row
DRAM is used to build external memory outside the processor chip
  Popularly known as the RAM of a computer
  Each address refers to a DRAM byte (4 GB DRAM requires a 32-bit address)

## Slide 35: Dynamic random access memory
The RAM of a computer is typically sold as dual-inline memory module (DIMM) cards
  Each card has several DRAM chips either on one side or on both sides of the card
Processor chip
(SRAM + logic)
DRAM controller
I/O
Devices
DRAM channels

## Slide 36: Dynamic random access memory
Organization of a DRAM chip
  Has several banks
  Each bank stores a 2D array of bits organized in rows and columns
  Doing a read or a write operation on a DRAM chip requires a bank number, a row address, and a column address
    The operation is done on the designated bank at the designated row and column
    The column address typically selects a few consecutive columns determining the output width or the column width of the chip (x4, x8, x16, etc.)
    Example: 512Mbit DRAM chip: 4 banks, 16K rows, 1K columns, x8

## Slide 37: Dynamic random access memory
Organization of a DRAM bank
  One wordline per row from the row address decoder
  The bits in a column are connected to a bitline through a bidirectional switch (also known as a pass transistor or an access transistor)
  The switch closes when the corresponding wordline goes HIGH; otherwise it is open

## Slide 38: Dynamic random access memory
Read operation to a DRAM bank
  The row address is sent first on the address bus along with a row address strobe (RAS) signal
  The command bus carries the command (e.g., read or write)
  The row address decoder generates the necessary wordline signal
  The wordline closes the switch and activates or opens the target row
    The bitlines are precharged at the midpoint of HIGH and LOW
    When the switch closes, the small difference in bitline voltage is sensed and magnified by an array of sense amplifiers

## Slide 39: Dynamic random access memory
Read operation to a DRAM bank
  After the row is activated or opened, the entire row is stored in a per-bank area called the row buffer
  Next the column address is sent on the address bus along with the column address strobe (CAS)
  The column address reads out one column worth (same as output width) of data and sends that on the DRAM channel
  It is possible to read out N consecutive columns from the row buffer without sending a new column address every time (except the first time), where N is the burst length of the DRAM module

## Slide 40: Dynamic random access memory
Read operation to a DRAM bank
  It is much faster to do CAS operations from the row buffer compared to precharging a bank and activating the row over and over
    Better to do all reads going to the same row of a bank first before changing row in that bank
Writes are similar, but requires data to be written
A double data rate (DDR) DRAM can transfer the data on both clock edges
  Two data tranfers in a cycle; hence called double data rate

## Slide 41: Dynamic random access memory
Organization of a DIMM card
  A bidirectional channel connects to a DIMM card for carrying data between the card and the memory controller (same as DRAM controller)
    Channel width is usually governed by standard interfaces
    JEDEC standards are the only accepted standard
      Joint Electron Device Engineering Council
    Channel width is usually 64 or 128 bits
  In addition to the data channel, there is an address bus and a command bus
    Unidirectional from memory controller to DIMM

## Slide 42: Dynamic random access memory
Organization of a DIMM card
  The chips in a DIMM card are divided into several ranks
  A read or a write command is sent to all the chips in a rank
    The chip selects of the chips in that rank are made HIGH
  The memory controller sends the same bank number, row number, and column number to all chips in the target rank
    The corresponding bank in each chip provide an output
    For example, with 64-bit channels and x4 chips, 16 chips constitute a rank

## Slide 43: Dynamic random access memory
Utility of burst length (BL)
  Typically a large chunk of data is fetched together by the processor from DRAM
    Tries to exploit spatial locality
    For example, 64 bytes in a large number of processors
  If BL is 8, an x4 DDR chip will generate four bits of output every half cycle after the first four-bit output
    Takes four cycles to complete the burst
    A rank of 16 chips will generate 64-byte output in four cycles after the first 64 bits
The first 64-bit output on a 64-bit channel may have a variable latency

## Slide 44: Dynamic random access memory
Variable latency of first element of a burst
  Read to already open/activated row: fastest
    Only need to send CAS with column address
    Known as row hit (10 to 20 ns)
  Read to a bank that has no open/active row
    Need to activate row and then send CAS
    Roughly 2x latency compared to fastest
    Known as row miss
  Read to a bank that has a different open row
    Need to close the row (precharge the bank)
    Need to activate new row and then send CAS
    Roughly 3x latency compared to fastest
    Known as row conflict

## Slide 45: Dynamic random access memory
After reading out the data from rank
  Transfer over the channel to the memory controller; adds more cycles to overall latency
  Transfer from memory controller to processor cache (an on-chip fast SRAM storage); even more cycles
    Stored for quick reuse in future
Address decoding in memory controller
  The processor sends read and write commands to the memory controller along with an address
    Writes need to carry data also
  The memory controller breaks this address down into channel, rank, bank, row, column

## Slide 46: Dynamic random access memory
Path between processor and DRAM
  Let us assume that the processor logic can request 32 bits of data at a time from the on-chip SRAM cache
    Referred to as the processor datapath width
    For example, for adding two 32-bit numbers, the processor will make two requests one after another to the cache
  Assume that the address width is 32 bits
    Need not be same as the datapath width and can be more or less
    Determines the maximum amount of DRAM that can be installed
      With 32-bit address, the maximum DRAM capacity is 4 GB

## Slide 47: Dynamic random access memory
Path between processor and DRAM
  Let us assume that the SRAM cache fetches 64 bytes of data at a time from DRAM
    Beneficial because of spatial locality
Processor logic
SRAM cache
32-bit
data
bus
32-bit
address
bus
Command
bus (read/
write)
ACT/
PRE/CAS
DRAM
Controller
64-byte data bus
32-bit addr. bus
Command bus
Read/Write
DIMM card
64-bit
data
ch.
Addr.
bus

## Slide 48: Dynamic random access memory
Path between processor and DRAM
  DRAM controller extracts row, rank, bank, column, channel numbers from the address it receives from the SRAM cache
  If a new row needs to be activated, the command is ACT (or RAS) and the address bus carries the rank, bank, row numbers
  If a bank needs to be precharged, the command is PRE and the address bus carries the rank and bank numbers
  If a column read/write needs to be done, the command is CAS and the address bus carries the rank, bank, and column numbers

## Slide 49: Dynamic random access memory
Address decoding in DRAM controller
  Each address corresponds to a DRAM byte
  DRAM controller receives an address from the SRAM cache and fetches the 64-byte chunk from DRAM containing that address
    Achieved by programming the BL to eight
    Within a bank, the column number is automatically incremented to burst out eight 64-bit chunks
  Usually the channel number is decoded from the bits right after the least significant six bits of the address covering 64 bytes of data
    Ensures parallelism across channels for consecutive 64-byte requests
    Ensures that a request is never split across channels

## Slide 50: Dynamic random access memory
Address decoding in DRAM controller
  Example decoding (assuming 64-bit channels):
  Interface to DIMM is eight-byte wide (64-bit ch.)
    Lower three bits of the address must be zero to make it aligned to eight bytes (a 128-bit ch. has 4 bits zero)
  Example: 4 GB DRAM, two 64-bit channels, 1Gb x4 DRAM chips, 32K rows, four banks, BL=8
    32-bit address
    2 GB per channel, which means 16 chips per channel
    One rank per channel, 2K columns (each 4 bits)
    Column-low=3 bits, Channel=1 bit, Column-high=8 bits, Bank=2 bits, Rank=0 bit, Row=15 bits
    Column-low is incremented internally in the DRAM chips to cover eight bursts
Column-low
Channel
Column-high
Bank
Rank
Row
000

## Slide 51: Dynamic random access memory
Error detection and correction in DRAM
  Densely packed DRAM bits can suffer from flips (0 becoming 1 or 1 becoming 0) for certain reasons
    For correct computation, it is important to detect such errors and possibly abort computation if the error cannot be corrected; need error correction code (ECC)
  Simple parity code can detect one-bit errors, but cannot correct any error
    Parity = Bitwise xor of data (no. of 1’s odd or even?)
    One parity bit is stored per DRAM byte: each DRAM address refers to nine bits of data+ECC
    Complex codes are needed to correct errors
    SECDED (single error correct double error detect) codes are very popular

## Slide 52: Finite state machines (FSMs)
Every digital design is a marriage of combinational logic and sequential logic
  Combinational logic does the computation
  Sequential logic implements the state/storage elements
    Any realizable design would have a finite number of state elements
    This leads to a finite number of states e.g., with n state elements (each storing one bit), 2n different states are possible
  A digital design with finite number of states is called a finite state machine (FSM)
    Every realizable digital design is an FSM

## Slide 53: Finite state machines (FSMs)
Each state can have an output value attached to it
  In a four-state FSM, these values could be 00, 01, 10, 11
At any point in time, the FSM is in one of its possible states
The state can change based on the input and the combinational logic
  For example, in a four-state FSM, the current state 10 can change to 11 on an input 0; the current state 10 can change to 00 on an input 1

## Slide 54: Finite state machines (FSMs)
Next state function
  A function that defines the state transitions when inputs are applied to the FSM
  In a four-state FSM, the function defines the new state when the current state receives a 0 or a 1 input; F: S x I  S
    Eight possible entries in the function: F(S0, 0), F(S0, 1), F(S1, 0), F(S1, 1), F(S2, 0), F(S2, 1), F(S3, 0), F(S3, 1) where S0, S1, S2, S3 are the four states
  We will be interested only in synchronous FSMs where the state changes take place on clock edges (after propagation delay)
    Clock is an implicit input to all FSMs of our interest

## Slide 55: Finite state machines (FSMs)
Next state function: an example
  F(S0, 0) = S0, F(S0, 1) = S1, F(S1, 0) = S1, F(S1, 1) = S2, F(S2, 0) = S2, F(S2, 1) = S3, F(S3, 0) = S3, F(S3, 1) = S0
  Usually a state diagram is used to represent the next state function
S0
S3
S1
S2
0
0
0
0
1
1
1
1

## Slide 56: Finite state machines (FSMs)
Output function
  The FSM can output a value based on its current state and input; G: S x I  N
  In a four-state FSM, there are eight possible output function entries
  Example: G(S0, 0) = red, G(S0, 1) = green, G(S1, 0) = blue, G(S1, 1) = black, G(S2, 0) = red, G(S2, 1) = green, G(S3, 0) = orange, G(S3, 1) = brown
  If the output function depends only on current state, the FSM is called a Moore machine
  If the output function depends only on current state and input, the FSM is called a Mealy machine

## Slide 57: Finite state machines (FSMs)
Next state function
(Combinational logic)
State registers
Output function
(Combinational logic)
Input
clock
Output

## Slide 58: Finite state machines (FSMs)
f
y
x
clk
Two-bit state: (x, y); four states: 00, 01, 10, 11
Suppose f(0) = 1 and f(1) = 0
00
11
01
10
0
1
1
initial
initial
0
1
1
1
1
0
0
1

## Slide 59: Finite state machines (FSMs)
f
y
x
clk
Two-bit state: (x, y); four states: 00, 01, 10, 11
Suppose f(0) = 1 and f(1) = 0
00
11
01
10
0
1
1
0
start
0
0
1
1
start

## Slide 60: Finite state machines (FSMs)
f
y
x
clk
If the environment is sampling the output only at y, the
output function depends only on the current state and
is equal to the y bit of the state

## Slide 61: Finite state machine design
Step#1: derive the FSM from problem description
  This is usually the challenging step
Step#2: decide the state elements
Step#3: design the combinational logic for the next state function
Step#4: design the combinational logic for the output function

## Slide 62: Finite state machine design
Example
  We would like to design a digital logic that detects if the input pattern is alternating i.e., the input is 101010… or 010101…
Start
S0
S1
T0
T1
Reject
x=0
x=1
x=1
x=0
x=0
x=1
x=0
x=1
x=1
x=0
x=0,1

## Slide 63: Finite state machine design
Example: detecting alternating input patterns
  Output of Reject state is 0 and of all other states is 1
    Could drive an LED with the output and the LED will keep glowing as long as the input alternates
    Empty and single-bit inputs are assumed to be alternating
  Six states require three state bits
    Call these a, b, c. Assume following state encoding:
    Start = 000 or ~a & ~b & ~c, S0 = 001 or ~a & ~b & c, S1 = 010 or ~a & b & ~c, T0 = 011 or ~a & b & c, T1 = 100 or a & ~b & ~c, Reject = 101 or a & ~b & c
    Output = ~Reject = ~a | b | ~c
      Includes states 110 and 111 also, but that is not wrong

## Slide 64: Finite state machine design
Example: detecting alternating input patterns
  Next step is to design the next state function
    Purely combination logic
    Can be designed by preparing a truth table where the inputs are current states and x and output is the next state
    The goal is to write down three combinational logic formulas that determine the D inputs to the three flip-flops storing a, b, c

## Slide 65: Finite state machine design
Example: detecting alternating input patterns
  Few truth table entries (da, db, dc are the D inputs of the a, b, c flip-flops)
  a,b,c,x=0,0,0,0 then da,db,dc=0,0,1 (this is S0)
  a,b,c,x=0,0,0,1 then da,db,dc=0,1,1 (this is T0)
Start
S0
S1
T0
T1
Reject
x=0
x=1
x=1
x=0
x=0
x=1
x=0
x=1
x=1
x=0
x=0,1

## Slide 66: Finite state machine design
Example: detecting alternating input patterns
  Next state function’s truth table may not have all entries fully specified
  In this example, the following four entries (out of sixteen) will not have any next state specified
  a,b,c,x=1,1,0,0
  a,b,c,x=1,1,0,1
  a,b,c,x=1,1,1,0
  a,b,c,x=1,1,1,1
  da,db,dc can be taken as anything (don’t cares) in these cases to simplify the combinational logic

## Slide 67: Finite state machine design
Example: detecting alternating input patterns
    a,b,c,x=0,0,0,0 da,db,dc=0,0,1 (this is S0)
    a,b,c,x=0,0,0,1 da,db,dc=0,1,1 (this is T0)
    a,b,c,x=0,0,1,0 da,db,dc=1,0,1 (this is Reject)
    a,b,c,x=0,0,1,1 da,db,dc=0,1,0 (this is S1)
    a,b,c,x=0,1,0,0 da,db,dc=0,0,1 (this is S0)
    a,b,c,x=0,1,0,1 da,db,dc=1,0,1 (this is Reject)
    a,b,c,x=0,1,1,0 da,db,dc=1,0,0 (this is T1)
    a,b,c,x=0,1,1,1 da,db,dc=1,0,1 (this is Reject)
    a,b,c,x=1,0,0,0 da,db,dc=1,0,1 (this is Reject)
    a,b,c,x=1,0,0,1 da,db,dc=0,1,1 (this is T0)
    a,b,c,x=1,0,1,0 da,db,dc=1,0,1 (this is Reject)
    a,b,c,x=1,0,1,1 da,db,dc=1,0,1 (this is Reject)

## Slide 68: Finite state machine design
Example: detecting alternating input patterns
  Next state function
  da = (~x & (c | a)) | (a & (b | c)) | (b & x)
  db = (a & b) | (~a & ~b & x) | (a & ~c & x)
  dc = ~c | a | (b & x) | (~b & c & ~x)
  Possible implementations of the next state combinational logic
    PLA (requires deriving the formulas)
    ROM (requires only the truth table): 12 rows x 3 bits
  If the next state function is implemented with a ROM, we can store the output function also in ROM and remove the output function logic
    One extra column of bits in the ROM for this example

## Slide 69: Finite state machine design
Next state function
(PLA or ROM)
a
~a | b | ~c
Input x
clock
Output (can drive an LED)
b
c
a, b, c
a, b, c
da
db
dc
x

## Slide 70: Finite state machine design
The output function, the next state function, and the states constitute the control unit of the FSM
The outputs of the FSM may drive the external datapaths
  In this example, the datapath is as simple as a discrete LED
  In more complex examples, the FSM outputs can be used as inputs to other computations

## Slide 71: Finite state machine design
Implementing next state function using a sequencer
  With an increasing number of states, it becomes difficult to design the next state function using PLA or ROM
  In many large FSMs, the states are often visited sequentially
    Appropriate state assignment can make it even more often
  In such FSMs, the next state function can be implemented using a simple counter with the option of “branching out” occasionally
    Branching happens when the next state is not current state + 1 or there are multiple possible next states

## Slide 72: Finite state machine design
PLA or ROM
Input
clock
Outputs
State registers
Increment
State selection logic
Branch control

## Slide 73: Finite state machine design
Implementing next state function using a sequencer
  The PLA or the ROM now implements the output function and the branch control
  The non-consecutive next states are handled by reading out the next state from separate ROMs in such cases
    These are called dispatch ROMs
    One dispatch ROM for each non-sequential case or all dispatch ROMs can be fused into one dispatch ROM
    Input decides the row of the dispatch ROMs

## Slide 74: Finite state machine design
PLA or ROM
Input
clock
Outputs
State registers
Increment
State selection multiplexor
Branch control
Dispatch ROMs

## Slide 75: Finite state machine design
Implementing next state function using a sequencer
  For the states, where the next state is just the incremented state, the branch control is stored as zero in the ROM
    Ensures that the incremented state will be selected by the multiplexor
  For each of the remaining states, the branch control specifies which dispatch ROM’s output should be selected
    Each dispatch ROM is indexed by the input and provides one output
  The ROM that stores the output function and the branch control is much smaller in width now

## Slide 76: Finite state machine design
Implementing next state function using a sequencer
  Each entry of the ROM that implements the outputs and the branch control is often seen as storing the instruction for controlling the next state and the output
    Referred to as a microcode ROM
    Each ROM entry is referred to as a microinstruction
    The state registers together form the microinstruction address or the microprogram counter which determines the ROM entry of the next microinstruction
  This style of FSM control implementation is known as microprogrammed control unit design