## Slide 1: Number Representation
Mainak Chaudhuri
Indian Institute of Technology Kanpur

## Slide 2: Sketch
Unsigned and signed integers
Overflow in integer operations
Floating-point numbers
Overflow in floating-point operations
Underflow in floating-point operations
Rounding modes

## Slide 3: Unsigned and signed integers
Numbers in a computer (or a processor) are represented in binary
  Digital designs are realized using devices such as transistors which can be made to operate at two discrete voltage levels representing 0 and 1 conveniently
  Number of bits devoted to represent a number is fixed by the design and cannot be extended after the design is finished
    Puts an upper bound on the value of the largest representable number in a computer
    If a computation generates a number that cannot fit within these bits, an overflow is said to have occurred

## Slide 4: Unsigned and signed integers
Non-negative integers (often called unsigned integers) can be represented using standard binary
Negative integers require the sign to be encoded appropriately
  Four possibilities have been tried: sign magnitude, two’s complement, one’s complement, biased
  Sign magnitude is the simplest: reserve the most significant bit to represent the sign of the integer
    Ambiguous representation of zero (00…0 and 100…0)
    Addition requires extra logic to set the result’s sign

## Slide 5: Representing negative integers
Sign magnitude representation
  With n bits to represent a number, the representable range is -2n-1+1 to 2n-1-1
Two’s complement representation
  Non-negative integers are represented as in sign magnitude representation
    MSB is 0 followed by the magnitude in n-1 bits
  An integer x and its negative add up to 2n
    x+(-x) = (2n – 1) + 1 or (-x) = (2n – 1) – x + 1
    Observe: (2n – 1) – x is same as bitwise inversion of x
    Offers an easy implementation to derive –x from x
      Invert bits of x to get y; add 1 to y; ignore carry out of MSB

## Slide 6: Representing negative integers
Two’s complement representation
  Unambiguous representation of zero (00…0)
  No special treatment needed by the sign bit
    To convert a two’s complement binary number to decimal use -2n-1 as the coefficient for the MSB and the rest is same as regular binary numbers
      Proof outline below:
      Consider an n-bit negative integer x in two’s complement representation: x=1bn-2bn-3…b1b0
      Therefore, -x in two’s complement representation is 0an-2an-3…a1a0 + 1 where ai = 1 – bi (follows from the definition of two’s complement)
      The decimal equivalent of –x is 1+ = 1+
      Therefore, the decimal equivalent of x is -1-

## Slide 7: Representing negative integers
Two’s complement representation
  No special hardware or step required in binary addition and subtraction (A+B or A-B)
    A and B are in two’s complement representation
    An extra array of xor gates to implement A-B
    Ignore carry out of MSB position
    Basic binary addition algorithm remains unchanged
  Only drawback is an imbalanced range on positive and negative sides
    Representable range: -2n-1 to 2n-1-1
Two’s complement representation is used in all computers today for handling integers

## Slide 8: Representing negative integers
Two’s complement adder/subtractor
  For A+B, the add/sub input wire is set to 0 and for A-B, the add/sub input wire is set to 1
  Both A and B must be in two’s complement representation (assumes n=4)
  Cout is usually ignored
    Actually used to detect overflows (will discuss later)
FA3
FA2
FA1
FA0
XOR
XOR
XOR
XOR
add/sub
Cout
Cin
S3
S2
S1
S0
a3
a2
a1
a0
b3
b2
b1
b0

## Slide 9: Representing negative integers
One’s complement representation
  An integer x and its negative add up to 2n – 1
    x+(-x) = 2n – 1 or (-x) = 2n – 1 – x
    Just bitwise inversion of x is –x
  Ambiguous representation of zero
    00…0 and 11…1
  How easy is addition or subtraction?
    Various cases have different treatments
    Not as easy as two’s complement addition/subtraction
  Balanced ranges on positive and negative sides
    -2n-1+1 to 2n-1 – 1

## Slide 10: Representing negative integers
Biased representation
  Representation of an integer x is x+bias
    x+bias is represented as a regular binary number with no sign bit
    bias is a constant fixed by the representation
  The goal is to avoid negative numbers all together i.e., x+bias ≥ 0
    Smallest representable number is -bias
  A typical bias is 2n-1 for n-bit representation
    An integer x is represented as x+2n-1 using unsigned binary representation
  Imbalanced range on positive and negative sides
    -bias to 2n – 1 – bias
    -2n-1 to 2n-1 – 1 when bias is 2n-1

## Slide 11: Representing negative integers
Use of two’s complement representation
  All computers use this representation
  The following C code can be used to verify whether a computer is using two’s complement representation for 32-bit integers (“int” type)
  int x = -10; // Any value can be used
  unsigned bits = *((unsigned*)&x);
  printf (“bits = %#x\n”, bits);
  Similarly, 64-bit integers (“long long” type) can be verified
  long long x = -10;
  unsigned long long bits = *((unsigned long long*)&x); printf (“bits = %#llx\n”, bits);

## Slide 12: Overflow in integer operations
Overflow occurs if the result of a computation cannot fit within the given number of bits
  In usual binary representation, if there is a carry-out in the MSB position of an addition, overflow is said to occur
  In two’s complement representation, overflow occurs if and only if the carry in to the MSB is different from carry out from the MSB
    Proof?
    Let the carry in to the MSB be cn-1 and carry out from the MSB be cn when adding two n-bit numbers

## Slide 13: Overflow in integer operations
Overflow in two’s complement addition
  Suppose that we are adding A (an-1an-2…a0) and B (bn-1bn-2…b0) both in two’s complement representation and let the sum be S (sn-1sn-2…s0)
  Case I: cn-1=0, cn=1
    Therefore, an-1=bn-1=1 and sn-1=0
    This is an overflow condition because adding two negative numbers cannot yield a positive number
  Case II: cn-1=1, cn=0
    Therefore, an-1=bn-1=0 and sn-1=1
    This is an overflow condition because adding two positive numbers cannot yield a negative number

## Slide 14: Overflow in integer operations
Overflow in two’s complement addition
  Consider adding A (an-1an-2…a0) and B (bn-1bn-2…b0) both in two’s complement representation and let the sum be S (sn-1sn-2…s0)
  Case III: cn-1=0, cn=0
    Therefore, at most one of an-1 and bn-1 is 1
    Case IIIA: an-1=bn-1=0
      Since cn-1 is 0, the magnitudes of two positive numbers are added without any overflow
      Therefore, there is no overflow
    Case IIIB: an-1=0, bn-1=1 (an-1=1, bn-1=0 is similar)
      Therefore, A+B = -2n-1 +
      Since cn-1 is 0, there is no overflow in adding lower n-1 bits of A and B; hence, sn-2sn-3…s0 =
      So, A+B = -2n-1 + sn-2sn-3…s0 = 1sn-2sn-3…s0 (no overflow)

## Slide 15: Overflow in integer operations
Overflow in two’s complement addition
  Consider adding A (an-1an-2…a0) and B (bn-1bn-2…b0) both in two’s complement representation and let the sum be S (sn-1sn-2…s0)
  Case IV: cn-1=1, cn=1
    Therefore, at most one of an-1 and bn-1 is 0
    Case IVA: an-1=1, bn-1=0 (an-1=0, bn-1=1 is similar)
      Therefore, A+B = -2n-1 +
      Since cn-1 is 1, the result of adding lower n-1 bits of A and B is 1sn-2sn-3…s0 = , where 1sn-2sn-3…s0 is treated as a positive value i.e., 2n-1 +
      So, A+B = -2n-1 + 1sn-2sn-3…s0 = -2n-1 + 2n-1 +
      = 0sn-2sn-3…s0
      Since in this case, an-1+bn-1+cn-1 = cn0, correct result is obtained by ignoring cn (hence, no overflow)

## Slide 16: Overflow in integer operations
Overflow in two’s complement addition
  Consider adding A (an-1an-2…a0) and B (bn-1bn-2…b0) both in two’s complement representation and let the sum be S (sn-1sn-2…s0)
  Case IV: cn-1=1, cn=1
    Therefore, at most one of an-1 and bn-1 is 0
    Case IVB: an-1=1, bn-1=1
      Therefore, A+B = -2n +
      Since cn-1 is 1, the result of adding lower n-1 bits of A and B is 1sn-2sn-3…s0 = , where 1sn-2sn-3…s0 is treated as a positive value i.e., 2n-1 +
      So, A+B = -2n + 1sn-2sn-3…s0 = -2n + 2n-1 +
      = -2n-1 + = 1sn-2sn-3…s0 in two’s complement
      Since in this case, an-1+bn-1+cn-1 = cn1, correct result is obtained by ignoring cn (hence, no overflow)

## Slide 17: Floating-point numbers
Real numbers are represented using scientific notation
  a.b x 10c
  Said to be normalized if there is only one non-zero digit to the left of the decimal point
    1≤a≤9
    Always possible to normalize a real number
Digital computers represent real numbers as floating-point binary numbers using normalized scientific notation
  1.b x 2c where b and c are binary numbers
  Binary point as opposed to decimal point

## Slide 18: Floating-point numbers
Normalized scientific representation
  Floating-point because the binary point can be moved by adjusting the exponent
How to convert a decimal real number to normalized scientific binary notation?
  Procedure for integer part: continued division
  Procedure for fraction part: continued multiplication
A representation of normalized floating-point number fixes the number of bits needed for b and c, given a fixed total number of bits
  Trade-off between range and precision
  If b has more bits then c has less

## Slide 19: Floating-point numbers
Normalized scientific representation has three advantages
  Simplifies exchange of floating-point data between computers due to a standard representation
  Simplifies floating-point arithmetic algorithms because all operands are in the same format
  Compacts the representation by discarding leading zeros on the left hand side
    0.0000000010101 is same as 1.0101 x 2-9 and it is enough to store b=0101 and c=-9
    b is referred to as the fraction (or mantissa) and c is referred to as the exponent

## Slide 20: Floating-point numbers
Normalized scientific representation
  IEEE 754 standard dictates the number of bits reserved for mantissa and exponent
    It is a standard format for representing floating-point numbers
    All computers are expected to follow this format
  A single-precision floating-point number is represented using 32 bits
    Sign magnitude representation
    MSB is sign bit
    Least significant 23 bits represent the mantissa
      24 bits of (1 + mantissa) represent the significand
    Middle eight bits represent the exponent

## Slide 21: Floating-point numbers
IEEE 754 single-precision format
  Exponent field needs to encode both positive and negative exponents
  Necessary to choose an encoding such that the entire 31-bit magnitude field is monotonic in the value of the floating-point number
    A larger magnitude floating-point number should have a larger 31-bit magnitude field compared to a smaller magnitude floating-point number
    Helps to sort numbers quickly by magnitude
    Mantissa is already monotonic in the value of the fraction
    Cannot use two’s complement encoding for exponent
      Negative exponents will be represented by large numbers

## Slide 22: Floating-point numbers
IEEE 754 single-precision format
  Biased encoding of exponent with bias set to 127
    Encoded exponent = 127 + actual exponent
    Actual exponent is allowed to range from -126 to 127 i.e., the encoded exponent can range from 00000001 to 11111110
    Encoded exponent cannot be 00000000 or 11111111 because these encodings are reserved to represent some special numbers
    Notice that larger encoded exponent now represents larger actual exponent because biased encoding preserves monotonicity
      Two’s complement encoding does not preserve monotonicity

## Slide 23: Floating-point numbers
IEEE 754 single-precision format
  Largest non-negative number
    +1.111…1 x 2127 = (2 – 2-23) x 2127
  Smallest positive number
    +1.000…0 x 2-126
  Negative number with smallest magnitude
    -1.000…0 x 2-126
  Negative number with largest magnitude
    -1.111…1 x 2127 = -(2 – 2-23) x 2127
0
11111110
11111111111111111111111
0
00000001
00000000000000000000000
1
00000001
00000000000000000000000
1
11111110
11111111111111111111111

## Slide 24: Floating-point numbers
IEEE 754 single-precision format
  Special numbers
    Encoding of zero (two possible representations):
    Encoding of +infinity:
    Encoding of –infinity:
    Encoding of NaN (result of 0/0, sqrt(-n), 0*inf, etc.):
X
00000000
00000000000000000000000
0
11111111
00000000000000000000000
1
11111111
00000000000000000000000
X
11111111
Anything non-zero

## Slide 25: Floating-point numbers
IEEE 754 single-precision format
  What about the numbers between 0 and ±N where N is the smallest representable magnitude (1.000…0 x 2-126)?
    These are called denormalized numbers because they are of the form ±0.b x 2c where c=-126
    Largest non-negative denormalized number:
      +0.111…1 x 2-126 = (1 – 2-23) x 2-126
    Smallest positive denormalized number:
      +0.000…01 x 2-126 = 2-149
    Negative denormalized range is similar
0
00000000
11111111111111111111111
0
00000000
00000000000000000000001

## Slide 26: Floating-point numbers
IEEE 754 single-precision format
  Representable magnitudes:
    0
    Denormalized: 2-149 to (1 – 2-23) x 2-126
    Normalized: 2-126 to (2 – 2-23) x 2127
    Infinity
      Anything with an exponent bigger than 127
      Note: a mantissa that is larger than the largest representable mantissa (i.e., 1111…1) does not make the magnitude infinity (will discuss this soon)
    NaN
Use of IEEE 754 single-precision format
  The C data type “float” translates to 32-bit single-precision format

## Slide 27: Floating-point numbers
Use of IEEE 754 single-precision format
  You can verify that the computer uses IEEE 754 single-precision format for float through the following code
  float x = -3.75; // Can use any float value
  // -3.75 = -11.11 = -1.111 x 21 in binary
  // biased exponent = 128, mantissa = 111000…0
  unsigned int sbit = ((*((unsigned int*)&x)) >> 31) & 1;
  unsigned int exponent = ((*((unsigned int*)&x)) >> 23)
  & 0xff;
  unsigned int fraction = (*((unsigned int*)&x)) & 0x7fffff;
  printf(“Sign bit: %u, biased exponent: %u, actual exponent: %d, mantissa: %#x\n”, sbit, exponent, exponent – 127, fraction);

## Slide 28: Floating-point numbers
IEEE 754 double-precision format
  Improves both precision and range over the single-precision format
  64-bit representation
    MSB is sign bit
    Least significant 52 bits represent mantissa
    The middle 11 bits represent biased exponent with a bias of 1023
      Actual exponent can range from -1022 to 1023
  Largest representable normalized magnitude
    1.111…1 x 21023 = (2 – 2-52) x 21023
  Smallest representable normalized magnitude
    1.000…0 x 2-1022 = 2-1022

## Slide 29: Floating-point numbers
IEEE 754 double-precision format
  Largest representable denormalized magnitude
    0.111…1 x 2-1022 = (1 – 2-52) x 2-1022
  Smallest representable denormalized magnitude
    0.000…01 x 2-1022 = 2-1074
  Zero
    Exponent = 0, Mantissa = 0
  Infinity
    Exponent = 11111111111, Mantissa = 0
  NaN
    Exponent = 11111111111, Mantissa = non-zero
Use of IEEE 754 double-precision format
  The C data type “double” translates to 64-bit double-precision format

## Slide 30: Floating-point numbers
Use of IEEE 754 double-precision format
  You can verify that the computer uses IEEE 754 double-precision format for double through the following code
  double x = -3.75; // Can use any float value
  unsigned int sbit = ((*((unsigned long long*)&x)) >> 63) & 1;
  unsigned int exponent = ((*((unsigned long long*)&x)) >> 52) & 0x7ff;
  unsigned long long fraction = (*((unsigned long long*)&x)) & 0xfffffffffffff;
  printf(“Sign bit: %u, biased exponent: %u, actual exponent: %d, mantissa: %#llx\n”, sbit, exponent, exponent – 1023, fraction);

## Slide 31: Floating-point numbers
IEEE 754 half-precision format
  Lower range and precision compared to single-precision for computers having narrow busses/operands
  16-bit representation
    MSB is sign bit
    Least significant ten bits represent mantissa
    The middle five bits represent the biased exponent with a bias of 15
      Actual exponent can range from -14 to 15
  Largest representable normalized magnitude
    1.1111111111 x 215 = (2 – 1/1024) x 215
  Smallest representable normalized magnitude
    1.0000000000 x 2-14 = 2-14

## Slide 32: Floating-point numbers
IEEE 754 half-precision format
  Largest representable denormalized magnitude
    0.1111111111 x 2-14 = (1 – 1/1024) x 2-14
  Smallest representable denormalized magnitude
    0.000…01 x 2-14 = 2-24
  Zero
    Exponent = 0, Mantissa = 0
  Infinity
    Exponent = 11111, Mantissa = 0
  NaN
    Exponent = 11111, Mantissa = non-zero

## Slide 33: Floating-point numbers
IEEE 754 quadruple-precision format
  Much higher range and precision compared to double-precision
  No computer supports it yet
  128-bit representation
    MSB is sign bit
    Least significant 112 bits represent mantissa
    The middle 15 bits represent the biased exponent with a bias of 16383
      Actual exponent can range from -16382 to 16383
  Largest representable normalized magnitude
    1.111…1 x 216383 = (2 – 2-112) x 216383
  Smallest representable normalized magnitude
    1.000…0 x 2-16382 = 2-16382

## Slide 34: Floating-point numbers
IEEE 754 quadruple-precision format
  Largest representable denormalized magnitude
    0.111…1 x 2-16382 = (1 – 2-112) x 2-16382
  Smallest representable denormalized magnitude
    0.000…01 x 2-16382 = 2-16494
  Zero
    Exponent = 0, Mantissa = 0
  Infinity
    Exponent = 111…1, Mantissa = 0
  NaN
    Exponent = 111…1, Mantissa = non-zero

## Slide 35: Overflow in floating-point ops
What happens if the magnitude of a floating-point number exceeds the largest representable by the corresponding format?
  E.g., float x > (2 – 2-23) x 2127
  May cause an overflow if exponent is larger than maximum allowed (e.g., 127 in single-precision)
    The number is treated as +infinity or –infinity depending on the sign of the number
  What if the fraction cannot fit within the mantissa field, but the exponent is within range?
    Not an overflow
    Handled by rounding the mantissa (default is round to nearest and round to nearest even for halfway round)
    Loss of precision

## Slide 36: Underflow in floating-point ops
What happens if the magnitude of a floating-point number is less than the smallest representable by the corresponding format?
  E.g., float x < 2-149
  May cause an underflow if an exponent smaller than the minimum (e.g., -126 in single-precision) is required to represent the number
    E.g., 2-150 in single-precision or 2-1075 in double-precision
    The number is treated as zero in this case
    Denormalized numbers are said to undergo gradual underflow as more and more leading zeros appear on the right side of the binary point ultimately becoming zero below 2-149

## Slide 37: Rounding modes
IEEE 754 rounding modes
  Round to nearest (default behavior)
    Round to nearest even for halfway rounding
      After rounding, the least significant representable mantissa bit should be even (see following single-precision examples)
    Example: 1.1111…1 (has 24 1s in mantissa) is rounded to 2.0 (in decimal) i.e., 1.0 x 21 in binary
    Example: 1.111…101 (has 22 1s followed by a 0 and a 1 in mantissa) is rounded to 1.111…10 (has 22 1s followed by a 0 in mantissa)
  Round toward zero
  Round toward +infinity
  Round toward –infinity
A computer can choose one of the modes