## Slide 1: Communicating with Environment
Mainak Chaudhuri
Indian Institute of Technology Kanpur

## Slide 2: Sketch
Input and output (I/O)
Interrupts
Direct memory access (DMA)
Exceptions
System calls

## Slide 3: I/O devices
A computer that can only execute instructions for computing and accessing memory is not very useful
  There is no way for the environment to give inputs to the computer or examine outputs of computation
A typical computer interfaces with a large number of I/O devices
  Keyboard, display, mouse, speaker, microphone, hard disk, printer, USB devices, etc.
  Need a mechanism to communicate with these devices
    How to read a key punch or how to display

## Slide 4: I/O devices
A typical I/O device has a set of command registers and a set of data registers
  These are assigned unique addresses and can be read or written to through load or store instructions
    Known as memory-mapped I/O registers
  To the computer, these appear as memory locations
    The only difference is that they are not in DRAM, but in I/O devices
  For example, printing something on the printer involves storing the data to be printed to the printer data registers and an appropriate command to the printer command registers

## Slide 5: I/O devices
Certain I/O commands send responses back to the computer
  A keyboard read needs to be conveyed to the computer
  Completion of a disk read needs to be conveyed to the computer
  Any read operation must be communicated to the computer
  To detect completion of a disk or keyboard read, one possibility is to continuously poll a register of the disk controller or the keyboard controller
    Wastes computer’s time (computer could do something else during this time)

## Slide 6: I/O devices
Polling works only if the computer is aware that it will receive some response from a certain I/O device
  Certain responses are accidental (e.g., ctrl+C to terminate a program or a mouse click)
    In such cases, the computer did not know beforehand and was not polling the memory-mapped register
An efficient solution that covers all cases is implemented using interrupts
  These are signals sent by the I/O devices to the computer
  For example, a key punch generates an interrupt

## Slide 7: Interrupts
Interrupts stop the normal instruction processing of a computer and make it execute an interrupt handler function
  Interrupts can be generated by hardware (e.g., I/O devices) or software (e.g., exceptions and system calls)
    MIPS treats all these as exceptions (any exceptional situation that interrupts normal instruction execution)
  There are two ways to implement interrupt or exception handlers
    Vectored interrupts or exceptions
    Cause-based interrupt handling (non-vectored)

## Slide 8: Vectored interrupts
Reserve an area of memory (outside user memory map) to store interrupt handlers
  Each interrupt is given a number and an array stores the starting addresses of the interrupt handlers
    Starting address of interrupt handler i is stored in IV[i]
    Assume that the interrupt number is in $1 and the starting address of array IV is in $3
    sll $2, $1, 2
    add $4, $3, $2
    lw $4, 0($4)
    jalr $4

## Slide 9: Vectored interrupts
The handlers stored at vector locations are usually very small
  These handlers further inspect the reason for the interrupt and jump to bigger interrupt service routines (ISRs)
    For example, all hardware interrupts are usually given a single number and they all call the same interrupt handler
    The interrupt handler finds out the source device of the hardware interrupt by consulting a special status register that stores the source/cause of interrupt
    The interrupt handler calls the appropriate ISR

## Slide 10: Non-vectored interrupts
MIPS implements non-vectored interrupts
  All interrupts jump to the same fixed location (0x80000180)
  MIPS maintains a status register and a cause register
    Status register encodes the source of interrupts (six hardware and two software interrupt levels)
    Cause register encodes the reason for interrupt (used mostly for software interrupts)
  The interrupt handler examines the status and cause registers and jumps to the appropriate ISR
ISR copies the input from I/O device data registers (e.g., keyboard buffer) to memory

## Slide 11: Direct memory access (DMA)
Copying large amounts of data from input devices to memory may take a significant amount of time
  Reading files from disk
Same applies to copying from memory to output devices
  Write to files on disk
Occupying the computer during this time wastes computer’s resources
  Could compute something useful during this time
Direct memory access (DMA) frees up the computer during data copying from/to I/O

## Slide 12: Direct memory access (DMA)
Computer initializes a specialized hardware called DMA controller by setting up the copy address range and the number of bytes to be copied
DMA controller does the actual copy operation
  DMA controller when copying from an input device sends the data to the DRAM controller for writing
  DMA controller when copying to an output device sends read requests to the DRAM controller
  When the copying completes, the DMA controller sends an interrupt to the computer to notify about the DMA completion

## Slide 13: Exceptions
Exceptions refer to situations where the running program exhibits unexpected behavior
  Arithmetic overflow, divide by zero, fetching and decoding an illegal opcode, accessing an illegitimate address or unaligned address (MIPS)
  In such situations, the PC of the offending instruction is saved in a register called exception PC (EPC) and the program counter is changed to point to a location that has a “trap” instruction
  The trap instruction allows the computer to enter the operating system which further invokes the appropriate exception handler after examining the cause register

## Slide 14: Exceptions
Some exceptions are restartable while some exceptions are not
  Restartable exceptions return to normal execution of the program by copying the EPC or EPC+4 (depending on the situation) into a general-purpose register ($X) and issuing a jr $X instruction after the exception handler completes
    Example: non-availability of code/data in memory (causes a page fault exception)
  Non-restartable exceptions typically lead to termination of the running program with an appropriate message printed on display
    Arithmetic exceptions, illegal opcode, crossing legitimate memory boundary, etc.

## Slide 15: System calls
System calls are pseudo-function calls to request access to certain hardware/software resources of the computer system
  Reading from a file on disk, reading from keyboard, writing to display, writing to a file, allocating dynamic memory, etc. involve system calls
  Some computers refer to system calls as software interrupts
  MIPS ISA has the syscall instruction for this purpose
    R format, has no operand, function 0xc
    Before invoking the syscall instruction, few registers need to be set up with appropriate information

## Slide 16: syscall instruction
Every system call has a number to indicate the purpose of the system call
  Reading from a file, writing to a file, allocating dynamic memory all have different system call numbers
  The system call number must be placed in register $v0 in MIPS
  A system call can accept four arguments in registers $a0, $a1, $a2, $a3
    More than four arguments can be passed by packing fourth argument onward in a structure and passing a pointer to the structure in $a3
  A system call returns any expected response in $v0

## Slide 17: syscall instruction
A syscall instruction executes by first changing the program counter to jump to a location
  Vectored implementations treat all system calls as software interrupts and all system calls are assigned a fixed location in interrupt vector array
  Non-vectored implementations jump to the same location for all kinds of interrupts
  The code in this location further examines $v0 and jumps to the appropriate system call handler
  System call handler accesses the argument registers and does the necessary things

## Slide 18: Examples of system call
Consider the read system call of UNIX
  Invoked as part of C library functions scanf, fscanf, read, etc.
    stdin is treated like a file
  Three arguments: $a0 should have file descriptor (a non-negative integer representing the file), $a1 should have destination memory buffer address, $a2 should have number of bytes to read
    Number of bytes to read is inferred from the data types of the arguments of the high-level function call
  SPIM simulator uses different system calls and conventions for reading from keyboard
    Only read_string requires buffer address and length in $a0 and $a1; other keyboard reads do not have args

## Slide 19: Examples of system call
Consider the read system call
  On return of a read system call, $v0 contains the number of bytes read
    Note that the actual bytes read can be found in memory starting from the address passed in $a1 to the system call
  SPIM uses a different convention for reading from keyboard: on return of a read system call for reading from keyboard, $v0 or $f0 (depending on type of data read) contains the actual value read (except for read_string, which does not have any return value)

## Slide 20: Examples of system call
Complete path of scanf
  C program calls scanf function
  Program jumps to scanf library function (jal)
  Sets up $v0, $a0, $a1, $a2
  syscall instruction executes (part of scanf func.)
  Invokes system call handler for reading from file
  Syscall handler goes to sleep until interrupted
  Keyboard punch generates interrupt to computer
  ISR wakes up system call handler
  Tail code of system call handler copies data from keyboard buffer to computer memory pointed to by $a1
  Returns to C program that called scanf

## Slide 21: Examples of system call
Consider the write system call
  Invoked as part of C library functions printf, fprintf, write, etc.
    stdout is treated like a file
  Three arguments: $a0 should have file descriptor (a non-negative integer representing the file), $a1 should have source memory buffer address containing the characters to be written, $a2 should have number of bytes to write
    Number of bytes to write is inferred from the data types of the arguments of the high-level function call
  SPIM simulator uses different system calls and conventions for writing to display
    Only argument is $a0 or $f12 holding the value to be printed ($a0 contains a pointer to string in print_string)

## Slide 22: Examples of system call
Complete path of printf
  C program calls printf function
  Program jumps to printf library function (jal)
  Sets up $v0, $a0, $a1, $a2
  syscall instruction executes (part of printf func.)
  Invokes system call handler for writing to file
  Copies data ($a2 bytes) from source buffer pointed to by $a1 to the display device’s memory
  Invokes the display device driver to actuate the low-level devices (CRT or LCD or LED) for printing the characters
  Returns to C program that called printf

## Slide 23: Examples of system call
Consider the sbrk system call used for allocating dynamic memory
  Invoked as part of C libray function malloc
  One argument: $a0 should contain the number of bytes to be allocated
  On return, $v0 contains the starting address of the allocated memory region

## Slide 24: Example of syscall in SPIM
SPIM assembly language program for printing the string “Hello World\n” to display
    .data
    msg: .asciiz "Hello World\n"
    .text
    .globl main
    main: li $v0, 4 # syscall 4 (print_str)
    la $a0, msg # argument: string address
    syscall # print the string
    jr $ra # retrun to caller

## Slide 25: Example of syscall in SPIM
SPIM assembly language program for reading an integer, adding 42 to it, and printing the result to display
    .text
    .globl main
    main: li $v0, 5 # syscall 5 (read_int)
    syscall
    addi $a0, $v0, 42 # print_int argument
    li $v0, 1 # syscall 1 (print_int)
    syscall # print the integer
    jr $ra # retrun to caller

## Slide 26: Example of syscall in SPIM
SPIM assembly language program for reading two floats, adding them, and printing the result to display
    .text
    .globl main
    main: li $v0, 6 # syscall 6 (read_float)
    syscall
    mov.s $f12, $f0 # return value in $f0
    li $v0, 6
    syscall
    add.s $f12, $f0, $f12 # print_float arg
    li $v0, 2 # syscall 2 (print_float)
    syscall # print
    jr $ra # retrun to caller

## Slide 27: Example of syscall in SPIM
SPIM assembly language program for reading ten integers, storing them in an array, adding them, and printing the result
      .data
      arrayX: .space 40
      msg: .asciiz "Sum of values: "
      endmsg: .asciiz "\n"
      .text
      .globl main
      main: addi $t0, $0, 10 # i  10
      la $t1, arrayX # $t1  arrayX
      loop: li $v0, 5 # syscall 5 (read_int)
      syscall
      sw $v0, 0($t1) # *arrayX  $v0
      addi $t1, $t1, 4 # arrayX++
      addi $t0, $t0, -1 # i--
      bne $t0, $0, loop

## Slide 28: Example of syscall in SPIM
      addi $t0, $0, 10 # i  10
      la $t1, arrayX # $t1  arrayX
      xor $t2, $t2, $t2 # sum  0
      loop1: lw $v0, 0($t1) # $v0  *arrayX
      add $t2, $t2, $v0 # sum  sum + $v0
      addi $t1, $t1, 4 # arrayX++
      addi $t0, $t0, -1 # i--
      bne $t0, $0, loop1
      li $v0, 4 # print_string
      la $a0, msg # argument: string
      syscall # print the string
      li $v0, 1 # print_int
      add $a0, $t2, $0 # int to print
      syscall
      li $v0, 4 # print_string
      la $a0, endmsg # argument: string
      syscall # print the string
      jr $ra # retrun to caller

## Slide 29: System calls supported by SPIM
print_int: no. 1, $a0 should have int value
print_float: no. 2, $f12 should have float value
print_double: no. 3, ($f12, $f13) should have double value
print_string: no. 4, $a0 should have the pointer to the string
print_char: no. 11, $a0 should have the ASCII value of char
sbrk: no. 9, $a0 should have the number of bytes to be allocated, return address in $v0

## Slide 30: System calls supported by SPIM
read_int: no. 5, return int value in $v0
read_float: no. 6, return float value in $f0
read_double: no. 7, return double value in ($f0, $f1)
read_string: no. 8, $a0 should have the destination memory buffer address, $a1 should have the length of the string
read_char: no. 12, return char value in $v0
exit: no. 10 (terminates the calling program)
exit2: no. 17 (terminates spim)

## Slide 31: System calls supported by SPIM
Also support system calls to open a file, read from a file, and write to a file
  Useful for programs operating on files