## Slide 1: Performance and Power
Mainak Chaudhuri
Indian Institute of Technology Kanpur

## Slide 2: Sketch
Abstract model of computer
Computer performance
Amdahl’s law
Benchmarks
Computer power
Moore’s law

## Slide 3: Abstract model of computer
Computer has an ISA
The implementation of the ISA is an abstract five-state synchronous FSM
  Each state change happens on posedge clock
  State 0: fetch the instruction pointed to by program counter from memory; update program counter to point to the next instruction
  State 1: decode the instruction to extract various fields and read source register operands
  State 2: execute the instruction in ALU; compute address of load/store instructions; update program counter if control transfer instruction
  State 3: access memory if load/store instruction
  State 4: write result to destination register if the instruction produces a result

## Slide 4: Abstract model of computer
Multi-cycle implementation of ISA
  Previous slide shows a five-cycle implementation
  Five states represent five stages of instruction processing
  Clock cycle time = longest stage latency
Equivalently, one could implement all five stages in a large single combinational logic
  Five stages would take one large single clock cycle
Two designs are almost equivalent
  We will further refine this statement later
  For now, you may assume any of the two implementations

## Slide 5: Abstract model of computer
In both models, complexity of the ISA can influence the clock cycle time
  If an instruction does a lot of things, that will lengthen the clock cycle time or may require more than five stages because execution of an instruction cannot be done in a single stage
    Increases average number of cycles per instruction if we keep the cycle time constant in a multi-cycle design
  Simple instructions can make clock cycle time smaller leading to high-frequency designs
Which one is better?
  Simple ISA with fast clock
    Simple ISA leads to more instructions in a program
  Complex ISA with slow clock
    Complex ISA leads to less instructions in a program
  Answer is not obvious

## Slide 6: Why measure performance?
Primarily two reasons
  To measure how good a computer is
  To understand why a computer is or is not performing as expected
Performance of a computer is a function of the performance of individual programs that run on the computer
A program’s performance is best measured as the reciprocal of its execution time
Equivalently, two computers’ performance on the same program can be compared by looking at the reciprocal of respective execution times

## Slide 7: CPI equation
How do we measure execution time? Which are the determinant factors?
Assume that we want to calculate the execution time of a program
  Execution time = Clock cycles to execute the progam × clock cycle time
  Executed clock cycles = number of executed instructions × average cycles per instruction
  Execution time = instruction count × CPI × cycle time
  Cycle time is also same as reciprocal of frequency (in appropriate unit)
  Execution time equally depends on three components

## Slide 8: CPI equation
Each component can be improved to get reduced execution time
  Reducing instruction count of a program normally depends on the instruction set of the processor and the smartness of the compiler e.g. separate equality check and branch instructions can be fused into one instruction such as bne or beq; similarly compiler can identify simple optimizations: ANDing with a mask and check instead of shift and AND and check
  Reducing CPI depends on the implementation of the ISA (known as microarchitecture)
  Frequency of a processor depends on semiconductor technology as well as the microarchitecture (not independent of CPI)

## Slide 9: CPI equation
Example
  Consider a processor that does not have a FPSQRT instruction and FPSQRT is emulated in software (large CPI)
  Frequency of FP instructions is 25%
  Average CPI of these instructions is 4.0
  Average CPI of non-FP instructions is 1.33
  Frequency of FPSQRT operation is 2%
  CPI of FPSQRT operation is 20.0
  One design alternative is to reduce CPI of FPSQRT to 2
  Other alternative is to reduce CPI of all FP operations to 2.0
  Which one is better?

## Slide 10: CPI equation
Solution
  Assume number of instructions = N, cycle time = t (in some unit)
  Timebase = (0.25 x 4 + 0.75 x 1.33)Nt = 2Nt
  Timedesign1 = Timebase – 0.02N x 20t + 0.02N x 2t = 1.64Nt
  Timedesign2 = (0.25 x 2 + 0.75 x 1.33)Nt = 1.5Nt
  Second design option is better

## Slide 11: CPI equation
Example
  For a computer, CPI of arithmetic instructions is 1, CPI of load/store instructions is 10, CPI of branch instructions is 3
  A program has 500 arithmetic instructions, 300 load/store instructions, 100 branch instructions
  Design optimization: ISA is expanded with new more powerful arithmetic instructions so that the number of arithmetic instructions in the program reduces by 25% and clock cycle time increases by 10%; is this design better?
  Without expanding the ISA, what if the arithmetic instruction CPI is improved? What is the maximum performance improvement?

## Slide 12: CPI equation
How to get these three parameters?
  CPU designers normally use simulators to get exact behavior of program execution
    Simulator is a piece of software that mimics the behavior of a computer
    SPIM is a simple MIPS simulator
    Simulators can be used to collect instruction count of a program and CPI
  A user can exploit the performance counters of a computer to get a rough estimate of time spent on certain code segments and the number of instructions in those segments
    Since frequency of a processor is known, these can be used to calculate CPI
  Static profiling of the assembly language program can provide some information about instruction distribution

## Slide 13: Amdahl’s law
Make the common case fast
  No point investing time and money to optimize part of a system that gets invoked few times
  Mathematical formulation:
    Suppose a program takes time t to execute on a processor
    A particular section of the program can be enhanced by some optimization in the processor; suppose x fraction of entire execution time is spent in this particular section of the program
    The optimization in the processor can speed up execution of this section by y times
    Therefore, overall speedup due to this optimization is
    t / tnew = t / (t – tx + tx/y) = 1 / (1 – x + x / y)
    Amdahl’s law says that as y approaches infinity, the speedup saturates at 1/(1 – x) i.e., effort should be invested in this optimization only if x is large

## Slide 14: Amdahl’s law
Look for portions of program that takes large amount of time to execute
  Allocate resources and design time proportionate to execution time
  As x increases the achieved speedup goes up for a fixed y; as y increases, speedup remains limited by x
  Amdahl’s law is usually used to compare design alternatives i.e. which design would bring more performance
  Example: FP square root is critical in graphics applications; two design choices: implement a FP square root hardware to improve sqrt execution by 10 times or improve all FP instructions by 2 times; suppose FP sqrt takes 20% of execution time while 50% time is spent in all FP instructions in the current processor; which design choice is better?

## Slide 15: Amdahl’s law
Amdahl’s law can be used to derive upper bound on achievable speedup in a parallel computer
  Suppose a sequential program takes time t to run on a single processor
  A fraction s of this time is spent in executing inherently sequential portions of the program
  The remaining time can be perfectly parallelized on arbitrary number of processors
  Maximum achievable speedup = t / (s*t + (1 – s)*t / P) which is 1 / (s + (1 – s) / P) on P processors
  In the limit, speedup gets capped at 1 / s
    Even if s is 0.05, speedup cannot be more than 20
    To get very large speedup, s should be tiny

## Slide 16: Performance comparison
Root of most debates and confusion
  Consider three computers A, B, C and programs P1, P2
  A executes P1 in 1 second and P2 in 1000 seconds
  B executes P1 in 10 seconds and P2 in 100 seconds
  C executes P1 in 20 seconds and P2 in 20 seconds
  Which computer is better?
  One possibility: calculate total time to execute P1 and P2, and compare them
  Along the same line it is possible to report arithmetic mean of the total time e.g. in this case 0.5(t(P1) + t(P2))
  On average A takes 500.5s, B takes 55s, C takes 20s to execute P1 and P2
  Is it a fair comparison? What could be wrong?
    Weighted AM is better?

## Slide 17: Benchmarks
Want to compare two processors by measuring their performance
  Need some standardized set of programs
  These are called benchmark programs
  Different types of computers have different focus: needs different set of benchmarks
    Performance metric for desktop/workstation is execution time (also known as response time)
    Performance metric for servers is throughput (number of jobs done per unit time with a limit on response time per job)
    Performance metric for embedded processors is also execution time with an emphasis on deadline and power consumption

## Slide 18: Desktop benchmarks
SPEC CPU is the standard
  Provided by Standard Performance Evaluation Corporation (SPEC) http://www.spec.org/
  Currently in the 6th generation: SPEC89, SPEC92, SPEC95, SPEC2000, SPEC2006, SPEC2017
  Has two types of programs: integer and floating-point to stress different CPU units (C, C++, Fortran)
  If you are introducing a new processor for desktop or uniprocessor workstation/server, you are supposed to report performance of all SPEC CPU 2017 programs
  For graphics performance two available benchmarks: SPECviewperf and SPECapc
  For Java run-time environment’s performance: SPECjvm

## Slide 19: SPEC CPU 2017 integer programs
10 applications covering a wide range
  perl (popular scripting language)
  gcc (part of GNU C compiler)
  mcf (public transit scheduling)
  omnetpp (discrete event simulation of ethernet network)
  xalancbmk (XML processing)
  x264 (video compression)
  deepsjeng (AI alpha-beta tree search in chess)
  leela (AI monte carlo tree search in go)
  exchange2 (AI recursive solution generator in sudoku)
  xz (general data compression)

## Slide 20: SPEC CPU performance
For each application, a computer’s performance is measured by a number known as the SPEC ratio
  SPEC provides the execution time of the application on a reference computer
  SPEC ratio is the reference execution time provided by SPEC divided by the execution time of the application on the target computer
  Further, the SPEC ratios of all the applications can be summarized by using a statistical sketch
    One popular way is to report the geometric mean (GM) of the SPEC ratios
    The computer having the largest geometric mean is the best for this set of applications
    Why GM? Comparison is independent of the reference time (think of SPECratio(C1)/SPECratio(C2) where C1 and C2 are two computers that you want to compare)

## Slide 21: Measuring computer power
Logic gates are built using transistors
When the output of a logic gate switches from 0 to 1 or 1 to 0, it generates current and charges or discharges the equivalent output capacitance of the gate
  Expends 0.5*C*V2 energy for each transition where C is the equivalent output capacitance (depends on the fan-out of the gate) and V is the supply voltage
  If number of such switching in the entire computer is N in a clock cycle, total energy expense per cycle is proportional to NCV2

## Slide 22: Measuring computer power
Power consumption is energy per unit time which is proportional to NCV2/cycle time or equivalently NCV2f where f is the clock frequency
Total energy expense of a program is NCV2t where t is the total number of cycles needed to execute the program
The energy expended in capacitive switching is known as the dynamic energy
Over generations of computers, transistor size has dropped leading to a drop in V
Frequency of designs has also increased

## Slide 23: Measuring computer power
Increase in f and drop in V may increase or decrease overall dynamic energy depending on the exact factors
  Even if it increases, it increases at a smaller rate compared to rate of increase in f
Drop in V has created a new problem called leakage current (also called static current)
  Caused by transistors that do not switch off completely even when doing nothing
  Creates a resistive path from supply to ground expending energy during inactive periods
  Expends leakage or static energy and increases in magnitude with decreasing transistor size

## Slide 24: Measuring computer power
Dynamic and leakage (or static) energy are big problems
Limits increase in clock frequency, limits complexity of logic, limits decrease in supply voltage with shrinking in transistor size
Leakage is a bigger problem because it grows exponentially with lowering of supply voltage
Many solutions today in computers
  Dynamically varying voltage and frequency depending on need
  Specialized circuits to arrest leakage current

## Slide 25: Moore’s law
Number of transistors in a given area doubles every 18 to 24 months
  Made possible by improved technology enabling shrinking of transistors
  More transistors means more smartness in the chip and hence, more performance
    Could design more sophisticate ALUs, for example
  Moore’s law has played a vital role in performance improvement of computers
  Negative side: switching more transistors every clock cycle increases power consumption leading to more heating (needs sophisticated cooling solutions)
    Moore’s law is said to have “slowed down” these days because of this reason