## Slide 1: Arithmetic Algorithms and ALU Design
Mainak Chaudhuri
Indian Institute of Technology Kanpur

## Slide 2: Sketch
Abstract model of computer
ALU architecture
Arithmetic algorithms
  Overflow detection in addition and subtraction
  Integer multiplication
  Integer division
  Floating-point addition
  Floating-point multiplication

## Slide 3: Abstract model of computer
Computer has an ISA
The implementation of the ISA is an abstract five-state synchronous FSM
  Each state change happens on posedge clock
  State 0: fetch the instruction pointed to by program counter from memory; update program counter to point to the next instruction
  State 1: decode the instruction to extract various fields and read source register operands
  State 2: execute the instruction in ALU; compute address of load/store instructions; update program counter if control transfer instruction
  State 3: access memory if load/store instruction
  State 4: write result to destination register if the instruction produces a result

## Slide 4: Abstract model of computer
Fetching an instruction requires accessing memory with the program counter as addr.
Decoding an instruction for MIPS is simple due to small number of formats and fixed position of the register specifiers
Reading operands from register file requires exercising the read ports
Executing an instruction and computing address of a load/store instruction requires an arithmetic logic unit (ALU)
Load/store instructions access memory with the computed address
Writing result to register file requires exercising the write ports

## Slide 5: Abstract model of computer
The logic on processor chip implements the FSM and the ALU
Processor chip
(SRAM + logic)
DRAM controller
DRAM channels
I/O
Devices

## Slide 6: Abstract model of computer
Processor logic
SRAM cache
32-bit
data
bus
32-bit
address
bus
Command
bus (read/
write)
ACT/
PRE/CAS
DRAM
Controller
64-byte data bus
32-bit addr. bus
Command bus
Read/Write
DIMM card
64-bit
data
ch.
Addr.
bus
FSM + ALU

## Slide 7: ALU architecture
ALU is responsible for executing the core of the MIPS instructions
  Everything except load/store instructions
ALU takes two inputs for most instructions and produces a result that may or may not get written to a destination register
  For example, control transfer instructions do not write to a general-purpose register, but writes to the program counter
ALUs are of two kinds: integer and floating-point
  The floating-point ALU is often referred to as the floating-point unit (FPU)

## Slide 8: Integer ALU architecture
Components of the integer ALU
  Adder/subtractor
    Executes add, addu, sub, subu, addi, addiu
    Computes target of conditional branch instructions
    Computes address of load/store instructions
  Multiplier
    Executes mult, multu
  Divider
    Executes div, divu
  Logic gate array
    Executes and, nor, or, xor, andi, ori, xori, lui
  Comparator and branch subunit
    Executes slt, sltu, slti, sltiu
    Executes the comparison part of beq, bne, bgez, bgtz, bltz, blez

## Slide 9: Integer ALU architecture
Components of the integer ALU
  Shifter
    Executes sll, sllv, sra, srav, srl, srlv
    Naïve implementation would shift by one bit position in every clock cycle
      Inefficient for arbitrary shift amounts
    Barrel shifters can shift an operand by arbitrary amount in time no more than an addition takes
  Multiplexer (part of branch subunit)
    Selects between branch target and PC+4 depending on the output of the comparison part of cond. branch
  Data movement unit (part of multiplier/divider)
    Executes mflo, mfhi, mtlo, mthi
  Some designs do not consider the shifter, multiplier, and divider as part of the ALU

## Slide 10: Overflow detection in MIPS
MIPS ISA offers two types of arithmetic instructions for addition and subtraction
  One type detects overflows (add, sub, addi) and the other doesn’t (addu, subu, addiu)
  Whether overflow should be detected in arithmetic operations is a part of the HLL specification
    MIPS ISA can support both types of HLLs
  If add/sub overflow is supposed to be detected, MIPS raises an exception on arithmetic overflow
    Saves PC in EPC
    Saves all general-purpose and floating-point registers in memory
    Jumps to a fixed handler which examines cause and status registers to invoke the appropriate exception handler

## Slide 11: Overflow detection in MIPS
Arithmetic overflow exception
  On completion of the handler
    Restore all general-purpose and floating-point registers from memory
    Compute EPC+4 and move it to $k0 or $k1 (same as $26 and $27)
      These two registers are reserved for use of operating system (e.g., interrupt, exception, system call handlers)
      These two registers are not preserved across handlers
    Execute jr $k0 or jr $k1 depending on where EPC+4 is
Overflow detection is also possible in software
  Not very relevant for MIPS addition/subtraction
  Important for processors that cannot detect overflow in hardware

## Slide 12: Overflow detection in software
Software cannot access the carry bits into and out of the most significant bit position
  So, cannot compare these to detect overflow
Observation
  In signed addition, an overflow is detected if and only if the operands have the same sign and the result has sign opposite of the operand
    If the operands have opposite signs, the result is guaranteed to have smaller magnitude than the larger magnitude operand and hence, there cannot be an overflow
  In signed subtraction, an overflow is detected if and only if the operands have opposite signs and the result has sign opposite of the first operand
    If the operands have the same sign, the result is guaranteed to have smaller magnitude than the larger magnitude operand

## Slide 13: Overflow detection in software
Code for detecting overflow in signed addition ($t0 = $t1 + $t2)
    addu $t0, $t1, $t2 # no overflow exception
    xor $t3, $t1, $t2
    slt $t3, $t3, $0 # $t3 is 1 iff signs of $t1, $t2 differ
    bne $t3, $0, no_overflow
    xor $t3, $t0, $t1
    slt $t3, $t3, $0 # $t3 is 1 iff signs of $t0, $t1 differ
    bne $t3, $0, overflow_handler
no_overflow: …

## Slide 14: Overflow detection in software
Unsigned addition and subtraction
  Overflow is detected if and only if the magnitude of the result exceeds the maximum representable unsigned value
    232 – 1 for 32-bit processors
Code for detecting overflow in unsigned addition ($t0 = $t1 + $t2)
    addu $t0, $t1, $t2 # no overflow exception
    nor $t3, $t1, $0 # $t3 has 232 - $t1 – 1
    sltu $t3, $t3, $t2 # $t3 has 1 iff $t1 + $t2 > 232 – 1
    bne $t3, $0, overflow_handler
  Note that the comparison must be unsigned (sltu) so that 232 - $t1 – 1 and $t2 are treated as unsigned operands

## Slide 15: Multiplication algorithm
One operand is called the multiplicand and the other is called the multiplier
  m-bit multiplicand and n-bit multiplier lead to (m+n)-bit product
Paper-pencil algorithm (assume unsigned operands)
    1001 multiplicand
    x 1010 multiplier
    ---------------------------------------------------------------
    0000
    1001 (why shift left?)
    0000
    1001
    ---------------------------------------------------------------
    1011010

## Slide 16: Multiplication algorithm
Paper-pencil algorithm (unsigned operands)
  Multiplicand = (am-1am-2…a0) = A
  Multiplier = (bn-1bn-2…b0) =
  Product = A.b0 + A.b1.2 + A.b2.22 + …
  The left shift operations are needed to take care of the multiplications by 2i
  The ith partial product = (bi ? A << i : 0)
  Leads to a simple multiplication algorithm that in each step produces one partial product by inspecting a bit position of the multiplier and accumulates the partial product into a product register
  We will refer to the ith bit of multiplier as multiplier[i]

## Slide 17: Multiplication algorithm
Multiplier[0] == 0 ?
Multiplicand  Multiplicand << 1
Product  Product + Multiplicand
Multiplier  Multiplier >> 1
Shift_amount++
Shift_amount == n ?
STOP
Multiplicand [m-1:0]
Multiplier [n-1:0]
Product [m+n-1:0]
Initial:
Product  0
Shift_amount  0
N
Y
Y
N

## Slide 18: Multiplication algorithm
(m+n)-bit multiplicand register
n-bit multiplier register
(m+n)-bit product register
(m+n)-bit adder
log n-bit shift amount
!= ?
<< 1
>> 1
+1
AND
n
clk
Clock inputs
Latency: n clk cycles
Clock cycle time =
max (adder, shifter,
incrementer latency)
AND
LSB

## Slide 19: Multiplication algorithm (simpler)
m-bit multiplicand register
(m+n)-bit {product,multiplier} register
m-bit adder
log n-bit shift amount
!= ?
>> 1
+1
AND
n
clk
Clock inputs
MUX
m’b0
LSB
m+n-1:n
m+n-1:n
Cout

## Slide 20: Faster multiplication
In the basic algorithm, n additions are done sequentially because we have used only one adder
Consider the following grouping
  Product = (A.b0+A.b1.2) + (A.b2.22+A.b3.23) + (A.b4.24+A.b5.25) + …
  The additions in the parentheses can be done in parallel after appropriately shifting the multiplicand (requires n/2 adders)
  The results of these n/2 additions can be further paired and combined in n/4 adders
  Overall, n – 1 additions would be arranged in a binary tree and the multiplication requires log2n cycles (can be done with n/2 adders)

## Slide 21: Signed multiplication
Negate the negative operands and do the multiplication
If the signs of the operands are opposite, negate the multiplication result
MIPS has both signed and unsigned multiplication
  mult instruction treats operands as signed
  multu treats operands as unsigned
MIPS offers no hardware support for detecting overflow in multiplication
  If needed, must be done in software

## Slide 22: Booth’s multiplication algorithm
Due to Andrew Booth [1951]
Handles both unsigned and signed operands
Basic observation
  Let the multiplicand be A and let the multiplier be bn-1bn-2…b0 = 000…011…100…0 where the block 1’s ranges from bp to bq with p < q
  Therefore, the multiplier is 2q+1 – 2p and the product is (A << (q+1)) – (A << p)
  Can be generalized by representing the multiplier as addition of disjoint blocks of 1’s
Append b-1 = 0 at the end of the multiplier
Assume that both multiplicand and multiplier are in two’s complement representation

## Slide 23: Booth’s multiplication algorithm
Algorithm
  Initialize product register to 0
  Scan the multiplier from b0 to bn-1
  When examining bi, if bi == bi-1, keep scanning
  When examining bi, if bi is 1 and bi-1 is 0, subtract (A << i) from product register
  When examining bi, if bi is 0 and bi-1 is 1, add (A << i) to the product register
  If i==n – 1, stop. Final product is in two’s complement representation.

## Slide 24: Booth’s multiplication algorithm
Observations
  In the worst case, needs n addition operations when the multiplier has an alternating bit pattern i.e., 0101…01
  If bn-1 is 1 (negative multiplier), the last operation done on the product would be a subtraction
    Will result in a positive product, if the multiplicand is also negative; otherwise the product is negative
Booth’s algorithm can be implemented in two stages
  First stage scans the multiplier and prepares the addition/subtraction operands
  Second stage does the additions and subtractions in a binary tree of adders as in the fast multiplication algorithm

## Slide 25: Division algorithm
Suppose dividend (A) = (am-1am-2…a0), divisor (B) = (bn-1bn-2…b0)
Problem statement: find Q and R such that A=BQ + R and R < B
  We will assume unsigned A and B to start with
  Clearly the maximum length of Q is m – n + 1 if m ≥ n; otherwise Q is 0 and R = A
  Mathematically, we want
  =
  The usual division algorithm proceeds by computing qi’s starting from the most significant bit i.e., qm-n

## Slide 26: Division algorithm
Steps in usual division algorithm
  1. Place A above B such that their most significant bits are aligned
    This may require shifting B to the left by m – n positions (equivalent to multiplying B by 2m-n)
    E.g., suppose A = 1001010, B = 1000 (m=7, n=4)
    A = 1001010
    B’ = 1000000 (shifted B)
  2a. If B’ is less than or equal to A, subtract B’ from A and assign Q = (Q << 1) | 1, A = the result of subtraction, B’ = B’ >> 1 (to compute next lower qi; notice the similarity with polynomial division)
  2b. If B’ > A, shift B’ to the right by one bit position and assign Q = (Q << 1) [Q gets a 0 bit]
  Repeat step 2a or 2b m – n + 1 times, each time producing one bit of Q; R is residual A at the end

## Slide 27: Division algorithm
Execution of the usual algorithm (iteration 1)
    A = 1001010 Q = 0
    B’ = 1000000
    --------------------
    0001010  new A Q = 1
    0100000  new B’

## Slide 28: Division algorithm
Execution of the usual algorithm (iteration 2)
    A = 0001010 Q = 1
    B’ = 0100000
    --------------------
    No subtraction
    0001010  A Q = 10
    0010000  new B’

## Slide 29: Division algorithm
Execution of the usual algorithm (iteration 3)
    A = 0001010 Q = 10
    B’ = 0010000
    --------------------
    No subtraction
    0001010  A Q = 100
    0001000  new B’

## Slide 30: Division algorithm
Execution of the usual algorithm (iteration 4)
    A = 0001010 Q = 100
    B’ = 0001000
    --------------------
    0000010  new A Q = 1001
    0000100  new B’
  Done executing four iterations (m – n + 1 iterations)
  Quotient is 1001 and remainder is residual A i.e., 10
Each iteration computes one coefficient qi (either 0 or 1) of the polynomial qi2i by equating the leading powers of residual A and B

## Slide 31: Division algorithm
The first step of aligning the divisor and dividend is important for the main division algorithm to work correctly
  In a processor, A and B will be in two 32-bit registers to begin with
  The first step requires computing m – n and shifting B to the left by m – n bits
  How to compute m and n quickly from A and B?
    This is essentially a search problem that searches for the most significant non-zero bit in a given binary string

## Slide 32: Division algorithm
Divisor  Divisor << (m – n)
Quotient  Quotient << 1
Remainder  Remainder – Divisor
Quotient  (Quotient << 1) | 1
Iteration++
Iteration == m – n + 1 ?
STOP
Initial:
Remainder  Dividend
Quotient  0
N
Y
Y
N
Divisor  Divisor >> 1
Remainder ≥ Divisor ?

## Slide 33: Division algorithm
Critical path of one iteration involves a comparison and a subtraction
  Left shift and OR, right shift, increment can all be done in parallel with subtraction
A variant of this algorithm always subtracts, then checks if the remainder is negative and if yes, restores the remainder
  Known as restoring division algorithm
  Checking if remainder is negative requires comparing only the most significant bit
  Critical path now involves a subtraction, a negative check, and an addition

## Slide 34: Restoring division algorithm
Divisor  Divisor << (m – n)
Quotient  Quotient << 1
Remainder  Remainder – Divisor
Quotient  (Quotient << 1) | 1
Iteration++
Iteration == m – n + 1 ?
STOP
Initial:
Remainder  Dividend
Quotient  0
N
Y
Y
N
Divisor  Divisor >> 1
Remainder < 0 ?
Remainder  Remainder + Divisor

## Slide 35: Non-performing restoring division
Divisor  Divisor << (m – n)
Quotient  Quotient << 1
Remainder  Remainder – Divisor
Quotient  (Quotient << 1) | 1
Iteration++
Iteration == m – n + 1 ?
STOP
Initial:
Remainder  Dividend
Quotient  0
N
Y
Y
N
Divisor  Divisor >> 1
Remainder < 0 ?
Remainder  Temp
Temp  Remainder
Lot less number of
arithmetic ops 
Two copy ops,
a subtraction,
a sign bit check
on critical path 

## Slide 36: Non-restoring division algorithm
Divisor  Divisor << (m – n)
Quotient  Quotient XOR 0x1
Remainder  Remainder – Divisor
Quotient  (Quotient << 1) | 1
Iteration++
Iteration == m – n + 1 ?
STOP
Initial:
Remainder  Dividend
Quotient  0
N
Y
Y
N
Divisor  Divisor >> 1
Remainder < 0 ?
Remainder  Remainder + Divisor
One extra step at end may be needed if Remainder is still negative

## Slide 37: Non-restoring division algorithm
Why is this correct?
  Suppose in iteration#k of restoring division, r – d turns out to be negative, so we restore r
  In iteration#k+1 of restoring division, we compute r – d/2 (note that d is shifted right)
  In non-restoring division’s iteration#k, we keep r – d (which is negative) and in iteration#k+1, we do r – d + d/2 yielding r – d/2, which is same as the value of the remainder in restoring division after iteration#k+1
  The quotient is adjusted in iteration#k+1 by first making the last shifted bit 0 and then shifting in a 1
Critical path = sign bit check; (addition or subtraction || Quotient update || divisor shift || iteration increment) [“;”  seq., “||”  parallel]

## Slide 38: Non-restoring division algorithm
Hardware implementation
  Directly follows from the algorithm
  It is possible to combine {remainder, quotient} in a single register of size m bits
    At the beginning, the entire register is occupied by the m-bit dividend and quotient is zero
    At the end, the least significant m – n bits along with the last quotient bit will be the final quotient and the remaining n bits will contain the remainder
    Justifies why Lo contains quotient and Hi contains remainder in MIPS division instructions’ result
    Key observation: instead of shifting the divisor to the right in each iteration, the same effect can be achieved by shifting the dividend to the left

## Slide 39: Division algorithm (A shifted left)
Execution of the usual algorithm (iteration 1)
    A,Q = 1001010 Q = 0
    B’ = 1000000
    ------------------------
    0001010 Q = 1
    0010101  new A,Q

## Slide 40: Division algorithm (A shifted left)
Execution of the usual algorithm (iteration 2)
    A,Q = 0010101 Q = 1
    B’ = 1000000
    --------------------
    No subtraction
    0101010  new A,Q Q = 10

## Slide 41: Division algorithm (A shifted left)
Execution of the usual algorithm (iteration 3)
    A,Q = 0101010 Q = 10
    B’ = 1000000
    --------------------
    No subtraction
    1010100  new A,Q Q = 100

## Slide 42: Division algorithm (A shifted left)
Execution of the usual algorithm (iteration 4)
    A,Q = 1010100 Q = 100
    B’ = 1000000
    -----------------------
    0010100 Q = 1001
  Done executing four iterations (m – n + 1 iterations)
  The remainder appears in upper 4 bits (n=4) of residual {A,Q} and quotient is the concatenation of the lower 3 bits (m – n = 3) of residual {A, Q} and the last bit of quotient
Remainder
Quotient = 1001

## Slide 43: Non-restoring division algorithm
Divisor << (m – n)
m-bit {remainder,quotient} register
m-bit adder /subtractor
Iteration count register
!= ?
<< 1
+1
AND
m – n + 1
clk
Clock inputs
XOR
MSB
m bits
OR
1
Add/
Sub

## Slide 44: Signed division
Suppose A and B are positive and we have A = BQ + R
So, -A = -BQ – R is the expected result of dividing –A by B
Rule: remainder must have the same sign as the dividend

## Slide 45: Signed division
Signed division algorithm
  Convert the negative operand(s) to their positive value(s) and use any unsigned division algorithm
  If both operands were positive originally, stop
    A = BQ + R
  If both operands were negative originally, negate remainder
    -A = -BQ + (-R)
  If dividend was negative and divisor was positive, negate both quotient and remainder
    -A = B(-Q) + (-R)
  If dividend was positive and divisor was negative, negate quotient
    A = -B(-Q) + R

## Slide 46: Signed division
MIPS has both signed and unsigned division
  div instruction treats operands as signed
  divu treats operands as unsigned
Faster division algorithms are non-trivial
  The subtractions cannot be done in parallel
  Fast algorithms try to predict quotient bits and detect and correct mispredictions on the fly

## Slide 47: Floating-point addition
Assume that the operands are represented in IEEE 754 format
Step 1: Align exponents of the operands by shifting significand of the smaller number to the right (recall significand = 1.mantissa)
Step 2: Add significands
  Use 2’s complement integer arithmetic ignoring the binary point
  If result is negative, convert to its positive value
  Put back the binary point after addition and assign the sign bit depending on the result’s sign
Step 3: Normalize the sum
  Shift right and increase exponent OR shift left and decrease exponent

## Slide 48: Floating-point addition
Step 4: If overflow or underflow detected, raise exception
Step 5: Round mantissa of the normalized sum to fit the precision
  This may make the result unnormalized e.g., 1.11111…1 in binary becomes 10.00000…0 after half-way rounding rule is applied
If not normalized, repeat steps 3, 4, 5; else stop
Precision could be lost in intermediate computations e.g., during shifting significand
  To avoid this, IEEE 754 standard recommends use of three additional bits in intermediate representations (guard bit, round bit, sticky bit)

## Slide 49: Use of guard, round, sticky bits
The guard and round bits extend the mantissa by two bits
The sticky bit appears after the round bit and is set to 1 if any bit to the right of the round bit is 1
These bits improve the precision of arithmetic whenever the significand needs to be shifted to the right
  These bits retain a few mantissa bits which would otherwise get dropped
If the normalization step needs to shift the significand to the left, these bits will start contributing to the precision of the mantissa

## Slide 50: Floating-point addition
Example: 0.5 + (-0.4375)
  0.5 = 1.000 x 2-1, -0.4375 = -1.110 x 2-2
Step 1: Align exponents
  -1.110 x 2-2 = -0.111 x 2-1
Step 2: Add significands
  1.000 + (-0.111)
  1000 + 1001 = 0001 (2’ complement)
  0.001 after putting back the binary point
Step 3: Normalize
  0.001 x 2-1 = 1.000 x 2-4 = 0.0625
  No overflow or underflow because exponent is within legitimate range; no need to round also

## Slide 51: Floating-point multiplication
Step 1: Add the biased exponents of the operands and subtract the bias to get the new biased exponent
Step 2: Multiply significands
  Use unsigned integer multiplication algorithm ignoring the binary point
  Put the binary point after N bit positions from right where N is the sum of the lengths of the mantissa of two operands
Step 3: Normalize the product
Step 4: If overflow or underflow detected, raise exception
Step 5: Round the product; if product is not normalized, repeat steps 3, 4, 5

## Slide 52: Floating-point multiplication
Step 6: If the signs of the operands are same, the product is assigned positive sign; otherwise the product is negative
Example: 0.5 x (-0.4375)
  (1.000 x 2-1) x (-1.110 x 2-2)
  New biased exponent = (127 – 1) + (127 – 2) – 127 = 124 = (127 – 3)
    Actual exponent -3
  Multiply significands: 1000 x 1110 = 1110000
    Put back binary point: 1.110000
  Unsigned product = 1.110 x 2-3
    Already normalized and no overflow
    No need to round
  Final product = -1.110 x 2-3 = -0.21875