## Slide 1: Memory Hierarchy and SRAM Cache Design
Mainak Chaudhuri
Indian Institute of Technology Kanpur

## Slide 2: Sketch
Abstract model of computer
Locality principle
Memory and storage hierarchy
Basics of SRAM caches
  Organization
  Protocol for cache lookup
  Cache hits and misses
Cache performance and AMAT equation
Multi-level cache hierarchy

## Slide 3: Abstract model of computer
Computer has an ISA
The implementation of the ISA is an abstract five-state synchronous FSM
  Each state change happens on posedge clock
  State 0: fetch the instruction pointed to by program counter from memory; update program counter to point to the next instruction
  State 1: decode the instruction to extract various fields and read source register operands
  State 2: execute the instruction in ALU; compute address of load/store instructions; update program counter if control transfer instruction
  State 3: access memory if load/store instruction
  State 4: write result to destination register if the instruction produces a result

## Slide 4: Abstract model of computer
Fetching an instruction requires accessing memory with the program counter as addr.
Decoding an instruction for MIPS is simple due to small number of formats and fixed position of the register specifiers
Reading operands from register file requires exercising the read ports
Executing an instruction and computing address of a load/store instruction requires an arithmetic logic unit (ALU)
Load/store instructions access memory with the computed address
Writing result to register file requires exercising the write ports

## Slide 5: Abstract model of computer
The SRAM cache on processor chip helps improve the average memory access time (AMAT)
Processor chip
(SRAM + logic)
DRAM controller
DRAM channels
I/O
Devices
Hard disks
Disk controller

## Slide 6: Abstract model of computer
Processor logic
SRAM cache
32-bit
data
bus
32-bit
address
bus
Command
bus (read/
write)
ACT/
PRE/CAS
DRAM
Controller
64-byte data bus
32-bit addr. bus
Command bus
Read/Write
DIMM card
64-bit
data
ch.
Addr.
bus
Hard disks
Disk controller
I/O hub
DMA controller

## Slide 7: Locality principles
Principles of locality exhibited by programs
  Code and data accessed now are likely to be accessed again in near-future
    Any interesting program would have loops and/or recursions
      Justifies why code and data accesses may be repeated
      Example: reuse of rows of A and columns of B when multiplying matrices A and B
    Known as temporal locality
  Code and data allocated close to the code and data being accessed now are likely to be accessed in near-future
    Sequential code access
    Sequential data access (e.g., walking over an array)
    Known as spatial locality

## Slide 8: Memory and storage hierarchy
Locality principles imply an important corollary
  Programs usually work on a small portions of code and data at a time
    The code and data needed over a time window of length t could be a subset of the code and data needed over a bigger time window of length t’
    Think about nested loops
This corollary is exploited to build a hierarchy of memory and storage structures
  Keep most recently used code and data close to the processor because this is needed now
  Keep increasingly larger supersets of code and data gradually away from the processor

## Slide 9: Memory and storage hierarchy
Why not keep everything in a large on-chip SRAM?
  Expensive and slow
Memory and storage parts are usually arranged in a hierarchy
  SRAM caches are closest to the processor logic, smallest in size, and fastest
    Total on-chip cache is usually few tens of MBs
  DRAM is outside processor chip, much larger in size, much slower than SRAM caches
    Tens to hundreds of GBs
  Hard disk holds everything, non-volatile, very large, very slow
    Tens to hundreds of TBs

## Slide 10: Memory and storage hierarchy
Hierarchical organization allows very fast access to a small subset of code and data needed now from the SRAM cache
Later this code and data can be exchanged to bring something else from DRAM
  SRAM caches have finite capacity, so something must be replaced to bring something new if the cache is already full
Also, code and data in DRAM can be swapped with something else from hard disk on demand
  Less frequent than exchange between SRAM and DRAM

## Slide 11: Memory and storage hierarchy
Example
State 0
IF
State 1
ID/RF
State 2
EX
State 3
MEM
State 4
WB
SRAM cache
DRAM
Hard disk
PC
PC
Load/Store address
N
Nx [t1]
N(1 – x)
N(1 – x)y
N(1 – x)(1 – y)
N(1 – x)(1 – y)
N(1 – x)(1 – y)
N(1 – x)y [t2]
N(1 – x)(1 – y) [t3]

## Slide 12: Memory and storage hierarchy
Example
  Suppose a program’s load/store instructions and instruction fetcher generate N memory accesses
  Nx accesses find the requested data in on-chip SRAM cache (x < 1)
  N(1 – x)y accesses find the requested data in DRAM (y < 1)
  Remaining accesses fetch data from hard disk
  An access to SRAM cache requires time t1 (hit)
  An access to DRAM requires time t2 (cache miss)
  An access to hard disk requires time t3
  Average access time = (Nxt1 + N(1 – x)yt2 + N(1 – x)(1 – y)t3)/N
    Since t1 << t2 << t3, as x and/or y increase(s), the average access time goes down

## Slide 13: Memory and storage hierarchy
Hard disk organization

## Slide 14: Memory and storage hierarchy
Hard disk organization
  Metal platters are coated with magnetic recording material and arranged vertically on a spindle
    One side or both sides of each platter can have recording capability
  Each platter or disk has a head for reading and writing data
  Each platter has concentric circles called tracks
  All heads read from the same track of all platters at the same time
    A particular track of all platters together forms a cylinder
  Each track is divided into small contiguous data chunks called sectors (of size 512 to 4096 bytes)

## Slide 15: Memory and storage hierarchy
Hard disk organization
  Anticipating good spatial locality in the running program, at a time a full sector is read out and filled in DRAM
    The read sector necessarily contains the data that was demanded by the processor logic
  Three components in accessing a target sector
    Move the head assembly of all platters to the correct cylinder
      Completely mechanical process and very slow
      The time required is known as the seek latency
    Rotate the platters to move the correct sector under the head
      Also mechanical and slow; adds rotational latency
    Read the sector and transfer to DRAM
      Adds transfer latency determined by read & copy bandwidths

## Slide 16: Basics of SRAM cache
Start with a simple design
  Array of code and data items
  A block is fetched at a time
    A block is a spatial segment of contiguous bytes
Code block
Code block
Data block
Code block
Data block
Data block
Data block
Data block
Code block
Block size

## Slide 17: Basics of SRAM cache
Start with a simple design
  Array of code and data items
  Any instruction or data element accessed will be fetched from DRAM and allocated a free slot in the cache, if it is not already in the cache
    Hope is that due to temporal locality, this item will be accessed soon and at that time, it will be found in the cache resulting in much shorter access time
    Drawback: doesn’t exploit spatial locality
  To exploit spatial locality, we could fetch a bigger block of code or data from DRAM containing the requested item
    Mimics what the hard disk to DRAM interface does
    Every SRAM cache fixes this fetch size and this is called the block size of the cache

## Slide 18: Basics of SRAM cache
Cache is looked up in two events
  State 0 of FSM generates an access for instruction using program counter as the address
  State 3 of FSM generates an access for data using the address computed in state 2
  Requested block is searched in the cache
    Needs to store the address along with each block
      Need to define block address (sequence number of a block)
      If block size is 2n bytes, block address is (Address >> n)
    Block address is the search key
    This searching time can be very large if done sequentially
    A parallel search would require a large number of comparators (equal to number of blocks in the cache)
      Would consume a lot of power and area

## Slide 19: Basics of SRAM cache
Start with a simple design
Code block
Code block
Data block
Code block
Data block
Data block
Data block
Data block
Code block
Block size
Block addr.
Block addr.
Block addr.
Block addr.
Block addr.
Block addr.
Block addr.
Block addr.
Block addr.
Address >> log2(Block size)
Search
Address is either the PC or the load/store address

## Slide 20: Basics of SRAM cache
If the looked up block is found in the cache, it is called a cache hit; otherwise it is a cache miss
  Cache miss requests are forwarded to the DRAM controller for further handling
  Eventually the DRAM controller will respond with the requested block and it will be allocated in the cache
    What if the cache is full?
      Needs to replace a block
    Which block to replace?
      Maybe the block that is not used recently (least-recently-used or LRU replacement algorithm)
      Maybe a random block (random replacement algorithm)
      LRU replacement requires keeping track of time of access
      Random replacement requires a random number generator

## Slide 21: Basics of SRAM cache
Cache hits need to be much faster than cache misses to be useful
To optimize the search time of a cache block, caches are typically organized as hash tables
  Each hash element has a block, a block address or tag, and a few state bits (e.g., valid/invalid)
  The blocks in a cache are logically divided into disjoint sets (these are hash buckets)
    Each set can have a maximum number of valid blocks
    This maximum number is known as the associativity of the cache
    For example, a 16 KB cache with 64-byte blocks can have 32 sets each with associativity 8

## Slide 22: 2-way set associative cache
TAG DATA
STATE
TAG DATA
STATE
TAG0
TAG1
Block address = {TAG,INDEX}; TAG bits can uniquely identify a block in a set
Set 0
Set 1
Set 2
Set k
2n bytes
2m sets
Way#0
Way#1

## Slide 23: Basics of SRAM cache
A cache with associativity A is often called an A-way set-associative cache
To look up a cache with an address
  The set index is first determined by passing the address through a hash function
  Within the set, the block addresses are searched in parallel for the target address
    Number of comparators is equal to the associativity of the cache (which is usually small)
  Critical path of lookup: determine set index, decode set index, read all block addresses in a set, parallel comparison, select at most one data block based on comparison outcome (needs a multiplexor)

## Slide 24: Basics of SRAM cache
Determining set index
  Many possible hash functions exist; we will discuss the simplest and the most popular one
  Suppose there are N sets in the cache
  To evenly distribute the block addresses among all sets, one possible mapping of block addresses to sets would map every Nth block address to the same set
    Set 0 gets block addresses 0, N, 2N, 3N, …
    Set 1 gets block addresses 1, N+1, 2N+1, 3N+1, …
  Set index can be determined by (block address) mod N
    N is always a power of two; therefore, (block address) mod N = (block address) & (N – 1) [avoids a division]

## Slide 25: 2-way set associative cache
TAG INDEX BLK. OFFSET
TAG DATA
STATE
Address
TAG DATA
STATE
TAG0
TAG1
Block address = {TAG,INDEX}; TAG bits can uniquely identify a block in a set
TAG0 and TAG1 are compared again TAG in parallel; at most one will match
Set 0
Set 1
Set 2
Set k
n bits
m bits
2n bytes
2m sets
Way#0
Way#1

## Slide 26: 2-way set associative cache
TAG INDEX BLK. OFFSET
TAG DATA
STATE
Address
TAG DATA
STATE
TAG0
TAG1
Set 0
Set 1
Set 2
Set k
n bits
m bits
DATA
ACCESS SIZE
(HOW MANY BYTES?)

## Slide 27: Basics of SRAM cache
Observations
  If associativity is one, number of sets is equal to the number of blocks in cache
    A given block address has a unique location in cache
    Known as direct-mapped cache (a given block address directly maps to a unique location in cache)
    Needs a single comparator and no multiplexing needed for data selection on critical path
      Faster hit time than set-associative designs
    Simple design, but may suffer from large number of collisions between blocks (known as conflicts)
      Block addresses 0, N, 2N, 3N, … all map to set 0 if there are N blocks in the cache
      Can increase the number of cache misses compared to a set-associative design
    This is the minimum possible associativity

## Slide 28: Basics of SRAM cache
Observations
  If associativity is equal to the number of blocks in the cache, then the number of sets is one
    Need to search all blocks in the cache during a lookup
      Restricts the number of blocks in the cache; otherwise too many comparators and a large multiplexor would be needed consuming power and area
    Known as fully associative cache (usually small in size)
    Since number of sets is one, there are no index bits and the entire block address is the tag
    Also, a given block can be placed anywhere in the cache
      Significantly reduces conflicts
    This is the maximum possible associativity for a given cache capacity
      Cache capacity = no. of blocks x block size = no. of sets x no. of ways x block size

## Slide 29: Basics of SRAM cache
Total number of bits in cache
  Data bits + Tag bits + valid bit = (Block size + Tag length + 1) x no. of sets x no. of ways
Observation
  For a fixed cache capacity, doubling of associativity halves number of sets
    Decreases set index bits by one and increases tag length by one (total number of address bits is constant)
    Number of comparators doubles, width of comparators increases by one bit, width of multiplexor increases by one bit
  For a fixed cache capacity and associativity, doubling of block size also halves the no. of sets

## Slide 30: Basics of SRAM cache
Example
  32-bit address, block size 64 bytes, direct-mapped, number of blocks (or sets) 512. Calculate the total number of bits in cache
  Tag length = 32 – 6 – 9 = 17 bits
  Tag and valid bits = 512 x 18 bits
  Total cache bits = 512 x (64x8 + 17 + 1) bits
Example
  32 KB cache with 64-byte block size and two ways. Calculate the size of the set index decoder.
  Number of sets = 32 x 210/(64 x 2) = 28
  Set index decoder size = 8 bits to 256 bits

## Slide 31: Basics of SRAM cache
Example
  32 KB fully associative cache with 64-byte block size. Calculate the data selection multiplexor and comparator widths. Assume 32-bit address.
  Number of ways = 32 x 210/64 = 29 = number of comparators
  Width of multiplexor = 512 to 1
  Tag length = 32 – 6 = 26 bits = comparator width

## Slide 32: Basics of SRAM cache
Handling writes to cache
  Store instructions write new data to cache; should DRAM be also updated immediately?
    If the DRAM is updated immediately, it is called a write-through cache
      Remember that the cache to DRAM controller interface is defined in terms of a cache block
      Modifying even one byte of a 64-byte cache block will require writing the whole block to DRAM
      Same byte or different bytes of the same block may be written multiple times
      Writes can also be done from a write buffer later
    Alternate option: write to DRAM only when a modified block is replaced from the cache
      Called a writeback cache; saves a lot of writes to DRAM
      Needs an extra bit per cache block to remember if the block has been modified; known as the dirty bit

## Slide 33: Basics of SRAM cache
Handling write misses
  A store instruction missing in a cache may or may not allocate the block in the cache
    If the block is not allocated in the cache, this protocol is known as no write-allocate; makes sense for write-through caches under the assumption that the block will not be accessed in near future
    If the block is allocated in the cache, this protocol is known as write-allocate; routinely used with writeback caches

## Slide 34: Cache performance
Definitions
  Hit rate = number of hits / number of accesses
    Bigger the better
  Miss rate = number of misses / number of accesses = 1 – hit rate
    Smaller the better
  Average memory access time (AMAT) = hit/miss detection time + miss rate x miss penalty
  Decreasing any of the three terms would improve AMAT
  Miss rate x miss penalty is often referred to as the memory stall time
  Overall execution time = CPU time + memory stall time

## Slide 35: Cache performance
To avoid interference between code and data, processors have separate caches for instruction and data
Example
  Icache miss rate 2%, Dcache miss rate 4%, processor CPI is 2 when memory stalls are ignored, miss penalty is 100 cycles, load/store instructions constitute 36% of all instructions. If the caches are made perfect (0% miss rate), what is the performance speedup?
    With perfect cache, CPI would be 2
    Actual CPI = 2 + 0.02 x 100 + 0.04 x 100 x 0.36 = 5.44
    Speedup = 5.44/2 = 2.72

## Slide 36: Cache performance
Techniques to improve hit/miss detection time
  Choose a simple design e.g., direct-mapped or low associativity
Techniques to improve miss rate
  High associativity or large capacity
    contradicts with low hit/miss detection time
  Larger block size
    Helps if program has spatial locality
    For fixed capacity and associativity, this reduces the number of distinct blocks in the cache and therefore, may increase miss rate beyond a certain block size
      A program may need a certain minimum number of blocks

## Slide 37: Cache performance
Techniques to improve miss penalty
  Early restart
    Start the processor as soon as the requested bytes arrive; no need to wait for the entire block
    The remaining bytes of the block will fill in the cache in background while processor continues execution
  Critical word first
    Configure DRAM module to return the 64-bit chunk containing the requested bytes in the first burst
    Combine it with early restart
  Multi-level cache hierarchy
    Put increasingly bigger and slower on-chip SRAM caches between processor and DRAM (better than going all the way to DRAM on a cache miss)

## Slide 38: Multi-level cache hierarchy
All commercial processors have two or three levels of SRAM cache on chip today
  L1 is the closest to the processor and L2, L3, … are further away, get gradually bigger and slower
  The levels are designed such that the latency of fetching a block from the last level SRAM cache is still much smaller than fetching from DRAM
    Typical sizes: L1: < 100 KB, L2: < 1 MB, L3: 2-32 MB
    Associativity typically increases with increasing level
    Block size may increase or may remain constant
    Typical round-trip latencies could be L1: <1 ns, L2: ~5 ns, L3: ~10 ns, DRAM: 50-100 ns
    Missing in last-level cache can be highly detrimental for performance

## Slide 39: Multi-level cache hierarchy
Processor FSM and logic injects code/data requests to L1 instruction/data cache
L1 cache hits are returned immediately to the processor; L1 cache misses are forwarded to the L2 cache
L2 cache hits are returned to the L1 cache, which forwards the requested bytes to the processor and also fills the block in L1 cache
  Future accesses can be satisfied from the L1 cache until the block is replaced from L1 cache
L2 cache misses are forwarded to L3 cache or DRAM depending on the number of SRAM cache levels

## Slide 40: Multi-level cache hierarchy
Example
  Processor with frequency 4 GHz and one level of SRAM cache, CPI 1.0 if all accesses hit in L1 cache, round-trip DRAM access latency is 100 ns, combined L1 miss rate per instruction is 2%. Calculate speedup if an L2 cache is added with round-trip access latency 5 ns and 25% miss rate per L2 access.
    Overall CPI of base processor = 1 + 0.02 x 100/0.25 = 9
    Overall CPI with L2 cache = 1 + 0.02 x 0.25 x 100/0.25 + 0.02 x 0.75 x 5/0.25 = 1 + 2 + 0.3 = 3.3
    Speedup = 9/3.3 = 2.72

## Slide 41: Multi-level cache hierarchy
Updated AMAT equation
  Average memory access time (AMAT) = L1 hit/miss detection time + L1 miss rate x L2 hit/miss detection time + L1 miss rate x L2 miss rate x L3 hit/miss detection time + L1 miss rate x L2 miss rate x L3 miss rate x DRAM fetch latency